Data Report No. 0103

William Lutter and Clifford Thurber

(University of Wisconsin-Madison)

1985 Kenya Rift International Seismic Project (KRISP 85)  Teleseismic Experiment

The 1985 Kenya Rift International Seismic Project (KRISP 85) teleseismic experiment consisted of two arrays (Figure 1), a 110 x 100 km two-dimensional array (Green et al., 1991) and a 500-km long E-W linear array (Dahlheim et al., 1985).  Both arrays crossed the central portion of the East Africa rift.  The University of Wisconsin-Madison segment, a 2-dimensional reconnaissance P-wave experiment, was designed to investigate a Bouguer gravity anomaly aligned along the rift axis.  Event data collected by the UW array are being made publicly available through the IRIS DMC as part of an NSF-supported project to archive historic UW-Madison digital seismic datasets collected by the research group of Prof. R. P. Meyer.  In addition, event data from the concurrent E-W linear array are provided with the UW array data.

The UW teleseismic experiment was positioned to overlay much of the KRISP 85 refraction experiment in order to use the refraction data to constrain teleseismic-derived velocity models (Green, 1993; Green and Meyer, 1992; Green et al., 1991).  The University of Wisconsin-Madison deployed fifteen 3-component digital seismographs in a 110 x 100 km array (Figure 1) from September 1 to December 15, 1985.  Twenty-three sites were occupied due to relocation of several seismographs (see Table 1 for locations of the UW stations).  During the 3 1/2 months of operation of the UW array, 84 teleseisms identified by the USGS (PDE) were recorded by 5 or more UW sites (Table 3).  Of these, 27 events with near-vertical incidence arrivals (PKP) were analyzed by Green and Meyer (1992).

The University of California Los Angeles (UCLA) simultaneously operated 17 seismograph stations deployed on the E-W linear array which traversed the UW array (Dahlheim et al., 1989).  Data from 12 of these sites (see Table 2 and Figure 1) are provided in this data report along with the UW instrumented data.  Dahlheim et al. (1989) report 40 good quality events were recorded by the UCLA E-W profile.  Data from 52 events are provided with this data report (see Table 4) including 22 events recorded by both arrays.

Data Collection and Processing

The University of Wisconsin instruments, equipped with HS10-1 1Hz natural frequency seismometers, were set to selectively trigger on teleseismic events and to record for 160 s at 50 samples/sec.    The data have been assembled in the form of day volumes containing events listed in Table 3.  The UW event data was preserved as SAC files containing station and timing information within the headers.   The UCLA instruments used were 8 UCLA Digital Cartridge tape recorders, 3 Lennartz PCM 5800 and 3 Sprengnether DR100.(Dahlheim et al., 1989) and were set to record at 20 samples/s.  Chronometers were checked every 4 to 8 days using traveling clocks set to Moscow radio time signals (Green, 1991).  SAC file headers contain timing, station, and event information.

Tape Provided

The data archive consists of one DAT tape with the event- and day-volume data (in SAC format), this report in postscript and RTF formats, and miscellaneous information.

UW Seismic Recorders

The University of Wisconsin-Madison portable digital seismic recorders are wide-dynamic-range instruments (106 dB) designed for recording seismic waves from earthquakes or explosions (Table 5) [Powell, 1983].  Data from 1-Hz Hall-Sears HS-10-1 geophones were recorded at 50-Hz sampling rates, with a 4-pole Butterworth anti-aliasing filter at 12.5 Hz.  A 13.6 kHz Omega receiver incorporated in each seismograph recorded data from the worldwide Omega navigational network concurrently with seismic signals.  A timing-correction process developed for application to the UW seismic recorders provides 1/4 sample rms time error relative to Universal Time [Schneider et al., 1987].  Ground motion may be estimated from an average value  for voltage sensitivity of 150 V/m/s for the UW Hall-Sears geophones.

Related publications:

Dahlheim, H., P. Davis, and U. Achauer, Teleseismic investigation of the East African Rift - Kenya, U. J. Afric. Earth Sci., 8, 461-470, 1989.

Green, W. Verney., Lithospheric Seismic Structure of the Cenozoic Kenya Rift and the Precambrian Midcontinent Rift from Teleseismic Tomography, Ph.D.. Thesis – University of Wisconsin-Madison, 178 pp., 1993

Green, W., and R. Meyer, Array observations of PKP phases across the Kenya Rift:  Implications for structure and tectonics, Tectonophysics, 204, 41-58, 1992.

Green, W., U. Achauer, and R. Meyer, A three-dimensional seismic image of the crust and upper mantle beneath the Kenya rift, Nature, 354, 199-203, 1991.

Powell, L.A., Engineering Description of the U.W. Portable Digital Seismograph, Proceedings of the Committee on Controlled Source Seismology (CCSS), Workshop on Portable Digital Seismograph Development, Los Altos, California, 121-122, 1983.

Schneider, J.F., R.C. Aster, L.A. Powell, and R.P. Meyer, Timing of portable seismographs from Omega navigation signals, Bull. Seismo. Soc. Am., 77, 1457-1478, 1987.

.

Figure 1.  Map of the 22 UW station (triangle) and 12 of 19 UCLA stations (circle) of the KRISP 85 Teleseismic Experiment are displayed in the lower panel.  The 84 teleseismic events recorded by the UW array (triangle) and 52 events recorded by the UCLA array (circle) are displayed in the upper panel.  Twenty-two events were recorded by both sets of instruments.  These 12 UCLA stations were available from UW tar tapes and are provided in this data report with the archiving of the UW instrumented KRISP85 teleseismic data set.

Table 1. Locations of UW stations deployed in KRISP85 Teleseismic Experiment.

| Station ID | Latitude | Longitude | Elev(m) | Name |
| --- | --- | --- | --- | --- |
| 1 | -1.438 | 36.657 | 1980 | Ngong |
| 2 | -1.493 | 36.481 | 1020 | Emerit |
| 3 | -1.349 | 36.137 | 1430 | Mosiro |
| 4 | -1.441 | 35.829 | 1850 | Narosura |
| 5 | -1.054 | 36.577 | 1750 | Mayer's |
| 6 | -1.058 | 36.285 | 1640 | Susaa |
| 7 | -1.160 | 35.917 | 1910 | Narok |
| 8 | -0.810 | 36.676 | 2500 | South |
| 9 | -0.787 | 36.285 | 1920 | Naivasha |
| 10 | -0.743 | 35.973 | 2770 | Suypeo |
| 11 | -0.824 | 35.906 | 2460 | Enabelibel |
| 12 | -0.584 | 36.635 | 2640 | North |
| 13 | -0.463 | 36.223 | 1790 | Elementeita |
| 14 | -0.463 | 36.036 | 2060 | Kiriri |
| 15 | -0.895 | 36.090 | 2880 | Melili |
| 16 | -0.744 | 36.262 | 1920 | Ndabibi |
| 17 | -0.524 | 36.667 | 3220 | Aberdare |
| 18 | -1.042 | 36.656 | 2220 | Uplands |
| 19 | -0.744 | 36.262 | 1920 | Melili |
| 20 | -1.264 | 36.099 | 1670 | Mosiro |
| 21 | -1.160 | 35.917 | 1910 | Narok |
| 22 | -1.507 | 35.756 | 2000 | Narosura |
| 23 | -1.058 | 36.255 | 1700 | Susua |

Table 2. Locations of UCLA stations deployed in the KRISP85 Teleseismic Experiment.

| StationId | Latitude | Longitude | elev(m) | Name |
| --- | --- | --- | --- | --- |
| K01 | -1.23517 | 35.023 | 1680 | Masai Mara |
| K01 | -1.23317 | 35.0257 | 1680 | After 10/11/85 |
| K02 | -1.18667 | 35.25 | 1780 | Aitong |
| K03 | -1.152 | 35.5833 | 1925 | Ngorengore |
| K04 | -1.12933 | 35.782 | 1920 | Narok |
| K06 | -1.08833 | 36.4243 | 1595 | Mt.Suswa |
| K10 | -0.9675 | 37.4727 | 1130 | Ekarakara |
| K11 | -0.964 | 37.7095 | 1100 | Kaewa |
| K12 | -0.831833 | 38.0855 | 960 | Mwingi |
| K13 | -0.83 | 38.339 | 770 | Nguni |
| K15 | -0.733 | 38.8095 | 570 | Katumba |
| K16 | -0.6275 | 39.2788 | 290 | Kzzz |
| K17 | -0.420833 | 39.6313 | 140 | Garissa |

Table 3. Locations of UW events recorded by the KRISP85 Teleseismic Experiment.

| Id | Name | m:d:yr | hr:mn:sc | latitude | longitude | Depth | Mag | # | Directory |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | fiji | 08:28:85 | 20:50:49.0 | -21.000 | -178.990 | 629 | 6.1 | 6 | W240 |
| 2 | s_sand | 08:29:85 | 06:13:10.8 | -57.243 | -025.333 | 50 | 5.6 | 5 | W241 |
| 3 | xinjia | 08:29:85 | 23:39:48.8 | 39.441 | 075.452 | 17 | 5.2 | 8 | W241 |
| 4 | nphili | 08:30:85 | 20:27:10.7 | 16.982 | 119.938 | 29 | 5.4 | 8 | W242 |
| 5 | yunnan | 09:01:85 | 19:07:42.2 | 23.769 | 102.738 | 10 | 5.0 | 8 | W244 |
| 6 | minaha | 09:01:85 | 22:25:34.1 | 00.665 | 121.430 | 83 | 5.1 | 9 | W244 |
| 7 | halmah | 09:03:85 | 23:32:47.5 | 01.409 | 128.153 | 114 | 5.7 | 10 | W246 |
| 8 | banda | 09:05:85 | 03:53:12.0 | -07.364 | 128.472 | 143 | 5.3 | 6 | W248 |
| 9 | tonga | 09:05:85 | 06:34:58.0 | -18.559 | -173.632 | 33 | 4.6 | 5 | W248 |
| 10 | ceram | 09:07:85 | 00:22:01.5 | -03.079 | 130.348 | 26 | 5.6 | 7 | W250 |
| 11 | ceram | 09:07:85 | 04:40:30.0 | -03.136 | 130.279 | 24 | 5.5 | 7 | W250 |
| 12 | greece | 09:07:85 | 10:20:50.2 | 37.445 | 021.235 | 31 | 5.3 | 8 | W250 |
| 13 | tonga | 09:11:85 | 17:47:31.0 | -15.350 | -173.540 | 30 | 5.8 | 10 | W254 |
| 14 | xinjin | 09:11:85 | 20:45:49.5 | 39.356 | 075.407 | 15 | 5.8 | 10 | W254 |
| 15 | sphili | 09:11:85 | 22:07:10.7 | 13.594 | 120.893 | 135 | 4.9 | 7 | W254 |
| 16 | oaxaca | 09:15:85 | 07:57:53.6 | 17.980 | -097.160 | 63 | 6.0 | 5 | W258 |
| 17 | tonga | 09:15:85 | 11:25:05.3 | -19.220 | -175.600 | 258 | 5.6 | 8 | W258 |
| 18 | tonga | 09:15:85 | 17:31:00.6 | -16.800 | -174.870 | 81 | 5.7 | 9 | W258 |
| 19 | sumba | 09:15:85 | 22:58:42.6 | -10.809 | 119.298 | 39 | 5.4 | 5 | W258 |
| 20 | tonga | 09:16:85 | 02:54:02.0 | -15.296 | -174.153 | 139 | 4.9 | 7 | W259 |
| 21 | iran | 09:18:85 | 00:10:34.8 | 31.627 | 049.447 | 33 | 5.2 | 5 | W261 |
| 22 | tonga | 09:19:85 | 08:06:21.0 | -18.060 | -175.540 | 302 | 4.9 | 7 | W262 |
| 23 | michoa | 09:19:85 | 13:17:50.1 | 18.540 | -102.553 | 29 | 6.4 | 8 | W262 |
| 24 | taiwan | 09:20:85 | 15:01:23.5 | 24.593 | 122.280 | 18 | 5.3 | 5 | W263 |
| 25 | guerre | 09:21:85 | 01:37:15.1 | 17.810 | -101.690 | 42 | 6.2 | 7 | W264 |
| 26 | snatla | 09:22:85 | 18:23:12.2 | 12.510 | -044.316 | 10 | 5.7 | 6 | W265 |
| 27 | banda | 09:24:85 | 20:28:52.4 | -06.405 | 130.037 | 147 | 5.6 | 9 | W267 |
| 28 | snatla | 09:25:85 | 07:06:45.7 | 12.443 | -044.333 | 10 | 5.3 | 6 | W268 |
| 29 | tonga | 09:26:85 | 04:16:22.0 | -16.000 | -173.200 | 41 | 4.7 | 8 | W269 |
| 30 | kermad | 09:26:85 | 07:27:47.0 | -34.610 | -178.570 | 16 | 6.4 | 12 | W269 |
| 31 | solomo | 09:27:85 | 03:39:08.8 | -09.810 | 159.850 | 33 | 6.2 | 9 | W270 |
| 32 | tonga | 09:27:85 | 10:10:15.9 | -22.179 | -174.600 | 11 | 6.2 | 9 | W270 |
| 33 | crete | 09:27:85 | 16:39:48.7 | 34.506 | 026.599 | 61 | 5.6 | 10 | W270 |
| 34 | tonga | 09:28:85 | 05:50:39.0 | -20.910 | -174.090 | 18 | 5.1 | 5 | W271 |
| 35 | yugosl | 09:28:85 | 14:50:15.2 | 41.581 | 022.254 | 7 | 5.0 | 9 | W271 |
| 36 | sphili | 10:01:85 | 10:01:44.8 | 13.669 | 120.766 | 119 | 4.6 | 5 | W274 |
| 37 | hind_k | 10:02:85 | 21:31:36.4 | 36.473 | 070.139 | 217 | 4.8 | 6 | W275 |
| 38 | afghan | 10:03:85 | 18:07:38.2 | 36.500 | 071.604 | 80 | 5.4 | 8 | W276 |
| 39 | malaga | 10:04:85 | 15:17:07.1 | -18.304 | 048.433 | 10 | 5.3 | 8 | W277 |
| 40 | canada | 10:05:85 | 15:24:02.2 | 62.237 | -124.226 | 10 | 6.5 | 12 | W278 |
| 41 | vanuat | 10:06:85 | 12:00:49.2 | -18.961 | 169.432 | 273 | 5.7 | 9 | W279 |
| 42 | java | 10:09:85 | 01:15:04.6 | -06.791 | 107.082 | 154 | 5.9 | 11 | W282 |
| 43 | alaska | 10:09:85 | 09:33:32.4 | 54.765 | -159.613 | 30 | 6.2 | 9 | W282 |
| 44 | fiji | 10:12:85 | 02:12:57.9 | -21.656 | -176.382 | 155 | 5.9 | 11 | W285 |
| 45 | el_sal | 10:12:85 | 20:29:20.8 | 13.154 | -089.720 | 42 | 5.4 | 5 | W285 |
| 46 | c_atla | 10:12:85 | 22:20:38.0 | 00.917 | -029.921 | 10 | 5.4 | 9 | W285 |
| 47 | tajik | 10:13:85 | 15:59:51.2 | 40.301 | 069.823 | 16 | 5.8 | 12 | W286 |
| 48 | nnatla | 10:18:85 | 01:44:28.9 | 56.757 | -034.119 | 10 | 5.2 | 5 | W291 |
| 49 | carlsb | 10:18:85 | 16:55:30.9 | 04.454 | 062.660 | 10 | 5.2 | 6 | W291 |
| 50 | sphili | 10:19:85 | 20:51:20.8 | 10.460 | 125.157 | 42 | 5.3 | 7 | W292 |
| 51 | kermad | 10:20:85 | 21:36:40.1 | -29.012 | -178.773 | 256 | 5.4 | 5 | W293 |
| 52 | java | 10:25:85 | 06:47:04.7 | -09.203 | 105.595 | 10 | 5.4 | 5 | W298 |
| 53 | banda | 10:25:85 | 18:12:19.5 | -07.077 | 124.284 | 596 | 5.9 | 8 | W298 |
| 54 | algeri | 10:27:85 | 19:34:57.1 | 36.460 | 006.761 | 10 | 5.5 | 9 | W300 |
| 55 | fiji | 10:27:85 | 22:35:18.0 | -17.717 | -178.835 | 565 | 5.4 | 7 | W300 |
| 56 | tanimb | 10:28:85 | 10:28:14.5 | -07.331 | 130.850 | 33 | 5.3 | 5 | W301 |
| 57 | tonga | 10:28:85 | 12:52:31.2 | -15.400 | -175.990 | 33 | 5.5 | 8 | W301 |
| 58 | sumatr | 10:29:85 | 05:19:26.4 | -05.713 | 103.110 | 33 | 5.2 | 8 | W302 |
| 59 | iran | 10:29:85 | 13:13:44.6 | 36.681 | 054.750 | 53 | 6.0 | 5 | W302 |
| 60 | tonga | 11:04:85 | 22:43:25.0 | -17.010 | -174.630 | 144 | 4.8 | 7 | W308 |
| 61 | s_sand | 11:06:85 | 08:15:39.6 | -58.716 | -026.223 | 132 | 5.7 | 8 | W310 |
| 62 | tonga | 11:06:85 | 22:16:16.9 | -16.370 | -173.270 | 50 | 5.1 | 8 | W310 |
| 63 | turkey | 11:07:85 | 08:26:21.4 | 40.310 | 042.307 | 33 | 5.1 | 7 | W311 |
| 64 | n_zeal | 11:07:85 | 19:12:31.8 | -35.210 | -179.320 | 49 | 6.2 | 9 | W311 |
| 65 | timor | 11:09:85 | 12:56:12.1 | -09.818 | 123.739 | 26 | 5.5 | 9 | W313 |
| 66 | greece | 11:09:85 | 23:30:42.9 | 41.262 | 023.988 | 22 | 5.4 | 9 | W313 |
| 67 | nsatla | 11:10:85 | 19:40:34.0 | -29.010 | -013.165 | 10 | 5.5 | 8 | W314 |
| 68 | nsatla | 11:14:85 | 02:11:45.6 | -28.912 | -013.109 | 10 | 5.3 | 7 | W318 |
| 69 | ssatla | 11:16:85 | 01:56:43.1 | -47.143 | -013.397 | 10 | 5.2 | 7 | W320 |
| 70 | m_indi | 11:16:85 | 04:12:18.8 | -38.577 | 078.368 | 10 | 5.8 | 7 | W320 |
| 71 | irian | 11:17:85 | 09:40:21.2 | -01.639 | 134.911 | 10 | 6.0 | 5 | W321 |
| 72 | nsatla | 11:18:85 | 18:18:34.7 | -32.298 | -013.364 | 10 | 5.4 | 6 | W322 |
| 73 | java | 11:20:85 | 02:49:44.8 | -10.449 | 111.817 | 33 | 5.1 | 7 | W324 |
| 74 | moluca | 11:21:85 | 02:27:18.7 | 02.374 | 126.729 | 68 | 5.4 | 7 | W325 |
| 75 | albani | 11:21:85 | 21:57:14.9 | 41.703 | 019.388 | 25 | 5.5 | 9 | W325 |
| 76 | s_sand | 11:24:85 | 21:32:41.8 | -59.450 | -024.842 | 37 | 5.3 | 5 | W328 |
| 77 | java | 11:25:85 | 16:26:30.4 | -08.649 | 108.495 | 68 | 5.1 | 5 | W329 |
| 78 | vanuat | 11:28:85 | 02:25:42.6 | -14.030 | 166.220 | 33 | 6.0 | 6 | W332 |
| 79 | vanuat | 11:28:85 | 03:49:55.5 | -13.980 | 166.100 | 43 | 6.2 | 6 | W332 |
| 80 | vanuat | 11:28:85 | 06:37:47.0 | -13.850 | 166.260 | 25 | 5.6 | 6 | W332 |
| 81 | at-ind | 11:30:85 | 02:28:11.5 | -29.235 | 061.253 | 10 | 5.6 | 6 | W334 |
| 82 | tonga | 11:30:85 | 03:04:18.8 | -16.366 | -174.197 | 165 | 5.7 | 6 | W334 |
| 83 | talaud | 12:14:85 | 06:46:11.7 | 03.683 | 126.600 | 22 | 5.8 | 5 | W348 |
| 84 | arabia | 12:14:85 | 18:13:31.5 | 14.712 | 057.999 | 10 | 5.5 | 6 | W348 |

Table 4. Locations of UCLA events recorded by the KRISP85 Teleseismic Experiment.

| evt | name | lat | lon | depth | yr | day | UW Id |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | eq8510192051 | 10.270 | 125.900 | 42.0 | 1985 | 292 | 50 |
| 2 | eq8510230049 | -11.600 | 125.900 | 14.0 | 1985 | 296 |  |
| 3 | eq8510250647 | -9.120 | 105.350 | 10.0 | 1985 | 298 | 52 |
| 4 | eq8510251812 | -7.400 | 124.170 | 596.0 | 1985 | 298 | 53 |
| 5 | eq8510281028 | -7.190 | 130.510 | 61.0 | 1985 | 301 | 56 |
| 6 | eq8510291313 | 36.400 | 54.450 | 53.0 | 1985 | 302 | 59 |
| 7 | eq8511021553 | 0.000 | 123.520 | 119.0 | 1985 | 306 |  |
| 8 | eq8511030357 | 23.350 | 91.300 | 33.0 | 1985 | 307 |  |
| 9 | eq8511030423 | 0.170 | 121.580 | 157.0 | 1985 | 307 |  |
| 10 | eq8511042123 | 13.400 | 120.110 | 77.0 | 1985 | 308 |  |
| 11 | eq8511060815 | -58.430 | -26.130 | 132.0 | 1985 | 310 | 61 |
| 12 | eq8511062216 | -16.110 | -173.190 | 33.0 | 1985 | 310 | 62 |
| 13 | eq8511071912 | -35.150 | -179.200 | 44.0 | 1985 | 311 | 64 |
| 14 | eq8511080838 | 6.370 | 124.900 | 46.0 | 1985 | 312 |  |
| 15 | eq8511091256 | -9.490 | 123.440 | 26.0 | 1985 | 313 | 65 |
| 16 | eq8511101940 | -29.000 | -13.900 | 10.0 | 1985 | 314 | 67 |
| 17 | eq8511102046 | -6.580 | 129.110 | 160.0 | 1985 | 314 |  |
| 18 | eq8511111216 | -3.200 | 129.440 | 73.0 | 1985 | 315 |  |
| 19 | eq8511121543 | 1.540 | 127.110 | 114.0 | 1985 | 316 |  |
| 20 | eq8511140211 | -28.540 | -13.600 | 10.0 | 1985 | 318 | 68 |
| 21 | eq8511150539 | 13.500 | -88.410 | 89.0 | 1985 | 319 |  |
| 22 | eq8511151035 | -47.130 | -13.230 | 10.0 | 1985 | 319 |  |
| 23 | eq8511160156 | -47.800 | -13.230 | 10.0 | 1985 | 320 | 69 |
| 24 | eq8511162330 | -38.340 | 78.220 | 10.0 | 1985 | 320 |  |
| 25 | eq8511181818 | -32.170 | -13.210 | 10.0 | 1985 | 322 | 72 |
| 26 | eq8511191403 | 28.400 | 128.520 | 135.0 | 1985 | 323 |  |
| 27 | eq8511200249 | -10.260 | 111.490 | 33.0 | 1985 | 324 | 73 |
| 28 | eq8511210227 | 2.220 | 126.430 | 68.0 | 1985 | 325 | 74 |
| 29 | eq8511212157 | 41.420 | 19.230 | 25.0 | 1985 | 325 | 75 |
| 30 | eq8511241042 | 9.100 | -40.370 | 10.0 | 1985 | 328 |  |
| 31 | eq8511242132 | -59.270 | -24.500 | 37.0 | 1985 | 328 | 76 |
| 32 | eq8511251626 | -8.380 | 108.290 | 68.0 | 1985 | 329 | 77 |
| 33 | eq8511260027 | 22.340 | 121.560 | 27.0 | 1985 | 330 |  |
| 34 | eq8511261005 | 24.800 | 125.100 | 21.0 | 1985 | 330 |  |
| 35 | eq8511261323 | 24.800 | 125.800 | 35.0 | 1985 | 330 |  |
| 36 | eq8511280349 | -13.590 | 166.110 | 33.0 | 1985 | 332 | 79 |
| 37 | eq8511281740 | -8.400 | 30.000 | 10.0 | 1985 | 332 |  |
| 38 | eq8511300304 | -16.220 | -174.110 | 165.0 | 1985 | 334 | 89 |
| 39 | eq8512010616 | -16.320 | 66.420 | 10.0 | 1985 | 335 |  |
| 40 | eq8512031242 | -11.190 | 118.150 | 33.0 | 1985 | 337 |  |
| 41 | eq8512072126 | 0.260 | 66.590 | 10.0 | 1985 | 341 |  |
| 42 | eq8512081335 | 30.550 | 86.350 | 37.0 | 1985 | 342 |  |
| 43 | eq8512081424 | 30.530 | 86.320 | 33.0 | 1985 | 342 |  |
| 44 | eq8512091158 | -5.390 | 105.490 | 148.0 | 1985 | 343 |  |
| 45 | eq8512121238 | -6.430 | 108.100 | 251.0 | 1985 | 346 |  |
| 46 | eq8512140646 | 3.410 | 126.360 | 22.0 | 1985 | 348 | 83 |
| 47 | eq8512141813 | 14.420 | 57.590 | 10.0 | 1985 | 348 | 84 |
| 48 | eq8512170013 | -36.000 | 53.300 | 10.0 | 1985 | 351 |  |
| 49 | eq8512170049 | -36.100 | 53.270 | 10.0 | 1985 | 351 |  |
| 50 | eq8512170654 | 24.530 | 67.230 | 33.0 | 1985 | 351 |  |
| 51 | eq8512171447 | 3.440 | 126.390 | 33.0 | 1985 | 351 |  |
| 52 | eq8512171456 | -4.270 | 128.250 | 228.0 | 1985 | 351 |  |

Table 5.  General specifications, University of Wisconsin-Madison digital 3-component recorders

DATA STORAGE:		5" reel 1/4" tape, 1800 feet		or	SCSI 3-1/2" disk

CAPACITY:			20 Mbyte					210 Mbyte

FORMAT:			4-track; 3-channel + error correction		multi-stream packet

DYNAMIC RANGE:		106 dB		Noise = 0.25 V P-P		Clipping = 0.05 V P-P

CALIBRATION:		Random binary sequence and step current applied to seismometer

coils through a bridge (at programmed start times)

PASSBAND:			Low end:  2 poles at 0.09 Hz

High end:  4-pole Butterworth at (0.25 * sample rate)

SAMPLE RATE:		25, 50, 100, 200, 400 samples/second

PRE-EVENT DELAY:	512, 1024, 2048 samples/channel

MODES:			Programmed and/or multiple-mode triggered

PROGRAMMING:		Time (ddd – hr:mn:sc), repeat interval and count for run,

calibrate, trigger arm and disarm (24 entries)

RUN TIMES:			Programmable to 1000 minutes in 1 sec steps with optional

programmed limits on total recording time for each mode

TRIGGER HARDWARE:	STA/delayed LTA ratio; broadband or teleseismic filtered

TRIGGER SOFTWARE:	Three frequency band Walsh transform filter to discriminate

teleseismic, regional, and noise; with independent run times

STATUS REVIEW:		Omega signal, time, configuration, schedules, number of events

recorded and time used for each mode, times of last 500 events,

seismometer period and damping

TIMING INTERNAL:	1 mHz TCXO, +/- 1 x 10-6 over temperature range

EXTERNAL:			13.6 kHz Omega VLF phase recorded with seismic data; worldwide

coverage (except Antarctica and central Greenland)

Post-processing time corrections:  +/- 1 x 10-8 oscillator error;

1/4 sample RMS time error relative to U.T.

POWER:			12.5 V DC +/- 20%

40 ma average current waiting for trigger

400 ma average current recording to tape

50 ma average current recording to disk

DIMENSIONS:		56 x 33 x 40 cm

WEIGHT:			22 kg

TEMPERATURE:		0 deg to 50 deg C normal range (tape operates to 0 deg C)

-20 deg to 70 dec C reduced spec. (disk operates to –20 deg C)

-40 deg to 80 deg C storage