## Slide 1: Taiwan 24-bit Real Time Seismic Data System
Central Weather Bureau
Yi-Jing Lo

## Slide 2: 24-bit seismic data system
High density of stations
High quality of data
Real time
Wide coverage
Data diversification
Distribution of stations
188 Sites
338 Instruments

## Slide 3
Station
Channel
Network
Location
Network | 
CWB_BH | Down hole seismic network
CWB_BB | Broadband seismic network
CWB_SMT | Smart24 seismic network
CWB_OBS | OBS seismic network
IRIS_JPN | JMA seismic network
IRIS_IU | Global seismic network
IRIS_HK | Hong Kong seismic network
IES_YMS | TVO seismic network
IES_BATS | IES broadband seismic network
IES_FJ | Fu Jien seismic network
Channel | 
Ch1~Ch3 | acceleration (HLZ，HLN，HLE)
Ch4~Ch6 | Short period (velocity) (HSZ，HSN，HSE)
Ch7~Ch9 | broadband (HHZ，HHN，HHE)
Location | 
01 | Surface
02 | Downhole
03 | Ocean Bottom seismometer

## Slide 4: Data Types
SP
FBA
BB
OBS
CWB Earthquake Center
Tainan
stations
YUS
MPLS
TVO
Fu Jien
Tou Cheng
ADSL
Internet
Outer net
Inner net

## Slide 5: Structure of 24-bit Seismic Network
SP
FBA
BB
OBS
Others
module
Data Receiving
Layer
Data Integrating
Layer
Data Applying
Layer
Seismisity
monitoring
Earthquake
reporting
Early
Warning
Tsunami
waining
CMT
Focal
Mechanism
Local
monitoring
Data Exchange
MPLS、ADSL、 optic fiber submarine cable 、microwave
Internet
Geophysical Database Managemant System (GDMS)
Earthworm
WaveServer
Ringserver
Ringserver

## Slide 6
import
Structure of 24-bit Seismic Network

## Slide 7
Monitoring All the Seismic Network
normal
unknown
broken
The list of the 24-bit situation
module
ring
Wave server

## Slide 8
Monitoring All the Seismic Network
Layer 1
Layer 2
Layer 3
module
Ring
Wave server

## Slide 9
Earthquake Early Warning (EEW)
P-wave auto-picking
Earthquake message
At least 6 stations
RMS less than 0.8.
Proceed updating procedure.
EEW report
Skip the first and second earthquake message
Take the third earthquake message as the first EEW report.
EEW update
Difference of location > 20 km
Difference of magnitude > 0.5
9
Large event
Small event
9

## Slide 10
Earthquake Early Warning (EEW)
Processing Time :
In-land 15.2 sec off-land 21.6 sec
EEW update report

## Slide 11: Thank you for your listening