Appendix 4 - SEG-Y 3.00 (IASPEI) - Definition of Headers

c- Start of FINAL segy.inc version 3.00 (IASPEI), January 25, 1993 ----

c

c Isa Asudeh, Geological Survey of Canada

c             1 Observatory Crescent

c             Ottawa, Ontario

c             Canada K1A 0Y3

c             Tel. 613-996-5757

c             Fax. 613-992-8836

c             e.mail asudeh@cg.emr.ca

c

c This file is an implicit definition of the SEGY format with additions

c for refraction work. It is based on the SEGY standard of Barry et al,

c Geophysics (1975) with extensions labelled SEGY_IASPEI

c for refraction work. This version has been checked and verified by

c the U.S. Geological Survey and the IRIS/PASSCAL Consortium and will

c be used for data exchange in North America.

c

c This format is primarily for the EXCHANGE of data between processing

c centers. All information that we consider to be  essential for the

c successful exchange of data are marked with a "R" in column 70:     R

c Items considered desirable are marked with a "D" in column 70:      D

c

c Some items have been added to facilitate disk

c storage in a SEGY type file.

c Items purely for tape use are labelled TAPE                  TAPE

c in column 62 items purely for disk user are

c labelled DISK, otherwise this field                          DISK

c is left blank.

c

c-Units:

c  Refraction ground velocities are

c  in nanometers/sec. We adopt the convention:

c    (tape data word)*(10**gc) = nanometers/sec;

c  where tape data word is the value in the trace

c  data block and gc is a two byte gain constant word

c  beginning in byte 121 of the trace header.

c

c-Dimensions:

c These may vary from system to system.

c SEGY allows no more than 32767

c samples per trace. Maximum number of bytes needed to

c hold a single trace and its header is:

c 131308 = (32767 samples)*(4 bytes per sample) + 240 bytes header.

c For TAPE we recommend that

c no more than 32767 bytes per trace be used (including

c 240 bytes for a header). This leaves space for

c 16728 two byte samples or 8139 4 byte samples per trace.

c Start of Declarations:

c

c Parameter Statements:

c

c      maximum number of bytes per trace

integer MAXLEN

parameter (MAXLEN = 131308)

c      maximum number of samples per trace

integer MAXSAM

parameter (MAXSAM = 32767)

c      EBCDIC/ASCII header length (bytes)

integer EBCDIC

parameter (EBCDIC = 3200)

c      Reel Header Length (bytes)

integer RHLEN

parameter (RHLEN = 400)

c      Trace Header Length (bytes)

integer THLEN

parameter (THLEN = 240)

c

c Dimension Statements:

c

c      SEGY reel identification header part 1

character*1  segy1a(EBCDIC)

c      SEGY reel identification header part 2

character*1  segy1b(RHLEN)

c      SEGY trace data block

character*1  segydb(MAXLEN)

c      SEGY trace header

character*1 thead(THLEN)

equivalence (segydb(1),thead(1))

c      real and integer data arrays

integer*2    idata(MAXSAM)

real*4       rdata(MAXSAM)

equivalence (segydb(241),idata(1),rdata(1))

c

c end of Declarations.

c

c

c---------------------------------------------------------------------+

c Reel Identification Header (total 400 bytes)    Starts here         |

c---------------------------------------------------------------------+

c

c Job identification number                     SEGY_STANDARD

integer*4    jobid

equivalence  (segy1b(1),jobid)

c Line number                                   SEGY_STANDARD         R

integer*4    lineno

equivalence  (segy1b(5),lineno)

c Reel number                                   SEGY_STANDARD  TAPE   R

integer*4    reelno

equivalence  (segy1b(9),reelno)

c Number of data traces per record              SEGY_STANDARD         R

c By "record" we mean gather

integer*2    ntrace

equivalence  (segy1b(13),ntrace)

c Number of auxilliary traces per record        SEGY_STANDARD         R

integer*2    nauxt

equivalence  (segy1b(15),nauxt)

c Sample interval in microseconds (this data),  SEGY_STANDARD         R

c See override for this value (sinto, bytes 117-120) for

c more precise presentation.

integer*2    sint

equivalence  (segy1b(17),sint)

c Sample interval in microseconds (in field)    SEGY_STANDARD

c See override for this value (sint2o, bytes 121-124) for

c more precise presentation.

integer*2    sint2

equivalence  (segy1b(19),sint2)

c No of samples per trace this data             SEGY_STANDARD         R

c The total number of samples per trace is also

c stored with each trace, so this word is not

c essential. It can be used to calculate

c record length for disk files.

c If number of sample per trace varies

c from trace to trace leave this as 0.

integer*2    nsam

equivalence  (segy1b(21),nsam)

c No of samples per trace in the field          SEGY_STANDARD

integer*2 nsamf

equivalence  (segy1b(23),nsamf)

c Data sample format code                       SEGY_STANDARD         R

c  1   IBM 370 floating point (4 bytes)         SEGY_STANDARD         R

c  2   Fixed point            (4 bytes)         SEGY_STANDARD         R

c  3   Fixed point            (2 bytes)         SEGY_STANDARD         R

c  4   Fixed point with gain  (4 bytes)         SEGY_STANDARD         R

c

integer*2    icode

equivalence  (segy1b(25),icode)

c No of traces per  CDP ensemble                SEGY_STANDARD

integer*2    ncdp

equivalence  (segy1b(27),ncdp)

c Trace sorting code                            SEGY_STANDARD         R

c      itsort=1     Shot Gathers                SEGY_STANDARD

c      itsort=2     CDP ensemble                SEGY_STANDARD

c      itsort=3     Single fold continuous      SEGY_STANDARD

c      itsort=4     Horizontal stack            SEGY_STANDARD

c      itsort=5     Receiver Gather             SEGY_IASPEI

c      itsort=6     Gathers Sorted By Distance  SEGY_IASPEI

c      itsort=7     Gathers Sorted By Azimuth   SEGY_IASPEI

c      itsort=0     No sort.                    SEGY_IASPEI

integer*2    itsort

equivalence  (segy1b(29),itsort)

c  Vertical sum code                            SEGY_STANDARD

c  vcode = n sum on n traces                    SEGY_STANDARD

integer*2    vcode

equivalence  (segy1b(31),vcode)

c Start sweep frequency (HZ)                    SEGY_STANDARD

integer*2    ssweep

equivalence  (segy1b(33),ssweep)

c End sweep frequency (HZ)                      SEGY_STANDARD

integer*2    esweep

equivalence  (segy1b(35),esweep)

c Sweep length in milliseconds                  SEGY_STANDARD

integer*2    sleng

equivalence  (segy1b(37),sleng)

c Sweep type                                    SEGY_STANDARD

c     stype=1  linear                           SEGY_STANDARD

c     stype=2  parabolic                        SEGY_STANDARD

c     stype=3  exponential                      SEGY_STANDARD

c     stype=4  other                            SEGY_STANDARD

c     stype=5  borehole explosive source        SEGY_IASPEI

c     stype=6  water explosive source           SEGY_IASPEI

c     stype=7  airgun source                    SEGY_IASPEI

c     stype=8  earthquake                       SEGY_IASPEI

c     stype=9  quarry_blast                     SEGY_IASPEI

integer*2    stype

equivalence  (segy1b(39),stype)

c Trace no of sweep channel                     SEGY_STANDARD

integer*2    nts

equivalence  (segy1b(41),nts)

c Sweep trace taper in milliseconds at start    SEGY_STANDARD

integer*2    stts

equivalence  (segy1b(43),stts)

c Sweep trace taper  in milliseconds at end     SEGY_STANDARD

integer*2    stte

equivalence  (segy1b(45),stte)

c Taper type                                    SEGY_STANDARD

c     ttype=1 linrst                            SEGY_STANDARD

c     ttype=2 cos**2                            SEGY_STANDARD

c     ttype=3 other                             SEGY_STANDARD

integer*2    ttype

equivalence  (segy1b(47),ttype)

c Correlated data traces                        SEGY_STANDARD

c     cort=1 no, 2=yes

integer*2    cort

equivalence  (segy1b(49),cort)

c Binary Gain recovered                         SEGY_STANDARD

c     bgr=1 yes, 2=no

integer*2    bgr

equivalence  (segy1b(51),bgr)

c Amplitude recovery methods                    SEGY_STANDARD

c     arm=1 none, 2=spherical, 3=AGC, 4=other

integer*2    arm

equivalence  (segy1b(53),arm)

c Measurement system                            SEGY_STANDARD         R

c     1=meters, 2=feet                          SEGY_STANDARD

integer*2    isys

equivalence  (segy1b(55),isys)

c Polarity                                      SEGY_STANDARD

c   ipol=1 upward case movement gives negative  SEGY_STANDARD

c   ipol=2 upward case movement gives positive  SEGY_STANDARD

integer*2    ipol

equivalence  (segy1b(57),ipol)

c Vibrator polarity code                        SEGY_STANDARD

integer*2    vpc

equivalence  (segy1b(59),vpc)

c     number of traces in the tape/file         SEGY_IASPEI

integer*2 notif

equivalence (segy1b(61),notif)

c attribute information

c attri=0    velocity data nanometers/s         SEGY_IASPEI

c attri=1    instantaneous velocity nanometers/sSEGY_IASPEI

c attri=2    instantaneous frequency milliHz    SEGY_IASPEI

c attri=3    instantaneous phase  degrees       SEGY_IASPEI

c attri=4    slowness (m/ms)                    SEGY_IASPEI

c attri=5    semblance (0-1000)                 SEGY_IASPEI

c attri=6    displacement nanometers            SEGY_IASPEI

integer*2 attri

equivalence (segy1b(63),attri)

c Mean amplitude of all samples in all          SEGY_IASPEI

c      traces in the file.

real*4 meanas

equivalence (segy1b(65),meanas)

c Domain of data                                SEGY_IASPEI

c       domain=0 time/distance

c             =1 fk

c             =2 tau-p

integer*2 domain

equivalence (segy1b(69),domain)

c Not in use from version 3.00.

c Set to 1 for compatibility.

integer*2 msexp

equivalence (segy1b(71),msexp)

c Reduction velocity in meter(feet)/sec         SEGY_IASPEI           R

integer*4   vred

equivalence (segy1b(73),vred)

c Seconds of window start time                  SEGY_IASPEI           R

real*4 wstart

equivalence (segy1b(77),wstart)

c Seconds of window end time                    SEGY_IASPEI           R

real*4 wend

equivalence (segy1b(81),wend)

c Minimum of all samples in the file.           SEGY_IASPEI

real*4    minass

equivalence (segy1b(85),minass)

c Maximum of all traces in the file             SEGY_IASPEI

real*4     maxass

equivalence (segy1b(89),maxass)

c Recording instrument type                     SEGY_IASPEI           R

c If instrument types in reel header and trace

c header are different, then the trace header value

c must be used.

c

c       =0 Not specified.

c       =1 EDA (Scintrex) PRS1

c       =2 USGS cassette

c       =3 GEOS

c       =4 Springnether

c       =5 Teledyne

c       =6 Kinemetrics

c       =7 SGR

c       =8 TERATEK

c       =9 EDA (Scintrex) PRS4

c       =10 MARS 88

c       =11 MARS 66

c       =12 PCM 5800

c       =13 REFTEK

c       =14 GEOSTORE

c       =100 Mixed data

integer*2 iinstr

equivalence(segy1b(93),iinstr)

c File creation date - Year                     SEGY_IASPEI           R

integer*2 cryear

equivalence(segy1b(95),cryear)

c File creation date - Month                    SEGY_IASPEI           R

integer*2 crmnth

equivalence(segy1b(97),crmnth)

c File creation date - Day                      SEGY_IASPEI           R

integer*2 crday

equivalence(segy1b(99),crday)

c Disk File format                                             DISK

c   pad first header record past 3600 to data length

c   =0 Reel Header is 3600 bytes, data has

c      variable length records.

c   =1 Reel Header is 3600 bytes,

c      data is padded to nnb bytes.

c   =2 Reel Header and data are padded to nnb bytes.

c      All data have the same length.

integer*2 padtyp

equivalence (segy1b(101),padtyp)

c Character code. Must use EBCDIC for tape exchange.

c        =1 EBCDIC                              SEGY_IASPEI    TAPE   R

c        =2 ASCII                               	       DISK

integer*2 ccode

equivalence(segy1b(103),ccode)

c File record length in bytes,                                 DISK

c    data are padded to nnb bytes.

c  if padtyp=1,

c       then nnb should be >= trhlen+data length in bytes)

c  if padtyp=2, t

c       then nnb should be >= max(3600,trhlen+data length in bytes)

integer*4 nnb

equivalence (segy1b(105),nnb)

c Byte order within words                                      DISK

c     1   ='00 01'x Most  Signicant Byte first.

c     2   ='02 00'x Least Significant Byte first.

c Default for tape is MSB. Default for disk depends on machine.

integer*2 bord

equivalence(segy1b(109),bord)

c Trace header length                                          DISK

c   traces on disk are stored with header length

integer*2 trhlen

equivalence(segy1b(111),trhlen)

c Max number of channels per seismograph        SEGY_IASPEI           D

integer*2 nchps

equivalence(segy1b(113),nchps)

c

c n.b. bytes 115-116 of Binary Reel ID are empty.

c

c Override for sample interval(this data; sint) SEGY_IASPEI           D

c This variable is related to variable sint bytes (17-18).

c If this variable is set to non-zero, it holds a more

c precise value than sint.

c

c This is the status table for the value of this variable:

c      Variable Name  Overrides  Value       Result

c      sinto          sint       0           No action

c      sinto          sint       < 0         Sample rate in samples per second

c      sinto          sint       > 0         Sample interval in Nanoseconds

c

integer*4 sinto

equivalence(segy1b(117),sinto)

c Override for sample interval(in field; sint2) SEGY_IASPEI           D

c This variable is related to variable sint2 bytes (19-20).

c If this variable is set to non-zero, it holds a more

c precise value than sint2

c

c This is the status table for the value of this variable:

c      Variable Name  Overrides  Value       Result

c      sint2o         sint2      0           No action

c      sint2o         sint2      < 0         Sample rate in samples per second

c      sint2o         sint2      > 0         Sample interval in Nanoseconds

c

integer*4 sint2o

equivalence(segy1b(121),sint2o)

c      Distance-Azimuth Calculation Algorithm   SEGY_IASPEI

c      0 = Not specified

c      1 = Sodano algorithm. The program utilizes the

c          Sodano and Robinson (1963) direct solution

c          of geodesics (Army Map Service, Tech Rep #7,

c          section IV).

integer*2 daca

equivalence(segy1b(125),daca)

c      Earth Dimension Code                     SEGY_IASPEI

c      0 = Not specified

c      1 = Fisher 1960

c      2 = Clark 1866

c      3 = Ref ellipsoid 1967

c      4 = Hayford Internationl 1910

c      5 = World Geodetic Survey 1972

c      6 = Bessel 1841

c      7 = Everest 1841

c      8 = Airy 1936

c      9 = Hough 1960

c      10= Fischer 1968

c      11= Clarke 1880

integer*2 edc

equivalence(segy1b(127),edc)

c

c n.b. bytes 129-398 of Binary Reel ID are empty.

c

c Format version number times 100               SEGY_IASPEI           R

c         =99 Version .99

c         =100 Version 1.0

c         =200 version 2.0

c         =300 version 3.0

integer*2 fvn

equivalence (segy1b(399),fvn)

c

c---------------------------------------------------------------------+

c Reel Identification Header (total 400 bytes)    Ends here           |

c---------------------------------------------------------------------+

c

c

c---------------------------------------------------------------------+

c Trace Identification Header (total of 240 bytes) Starts here        |

c---------------------------------------------------------------------+

c

c Trace sequence number within line             SEGY_STANDARD         R

integer*4 tsnl

equivalence (thead(1),tsnl)

c Trace sequence number within tape             SEGY_STANDARD         R

integer*4 tsnt

equivalence (thead(5),tsnt)

c Original field record number                  SEGY_STANDARD         D

c Sequential Shot Number                        SEGY_IASPEI

integer*4 ofrn

equivalence (thead(9),ofrn)

c Trace number withint original field record    SEGY_STANDARD         R

c Receiver Site Number                          SEGY_IASPEI

integer*4 tnofr

equivalence (thead(13),tnofr)

c Energy source point number                    SEGY_STANDARD         R

c Shot Site Number                              SEGY_IASPEI

integer*4 espn

equivalence (thead(17),espn)

c CDP number                                    SEGY_STANDARD

integer*4 cdp

equivalence (thead(21),cdp)

c Trace number within CDP                       SEGY_STANDARD         R

integer*4 tncdp

equivalence (thead(25),tncdp)

c Trace identifications code                    SEGY_STANDARD         R

c     tic=1 seismic data                        SEGY_STANDARD

c     tic=2 dead                                SEGY_STANDARD

c     tic=3 dummy                               SEGY_STANDARD

c     tic=4 time break                          SEGY_STANDARD

c     tic=5 uphole                              SEGY_STANDARD

c     tic=6 sweep                               SEGY_STANDARD

c     tic=7 timing                              SEGY_STANDARD

c     tic=8 water break                         SEGY_STANDARD

c     tic=11 --> tic=20 component number + 10

c                       for multi-compnent data SEGY_IASPEI

c     e.g. tic=11 (vertical component, horizontals following);

c          tic=12 (North-South component of 3 component);

c          tic=13 (East-West component of 3 component).

c     tic=100 calibration pulse                 SEGY_IASPEI

c     tic=101 calibration Frequency             SEGY_IASPEI

c              /Amplitude/Phase triplets

c

integer*2 tic

equivalence (thead(29),tic)

c Number of vertically summed traces            SEGY_STANDARD

c yeilding this trace

integer*2 nvs

equivalence (thead(31),nvs)

c Number of horizontally stacked traces         SEGY_STANDARD

c  yeilding this trace

integer*2 nhs

equivalence (thead(33),nhs)

c Data use   (1=productions, 2=test)            SEGY_STANDARD

integer*2 duse

equivalence (thead(35),duse)

c Distance from source to receiver (meters)     SEGY_STANDARD

integer*4 idist

equivalence (thead(37),idist)

c Receiver group elevation                      SEGY_STANDARD

integer*4 irel

equivalence (thead(41),irel)

c Surface elevation of source                   SEGY_STANDARD

integer*4 ishe

equivalence (thead(45),ishe)

c Source depth                                  SEGY_STANDARD

integer*4 ishd

equivalence (thead(49),ishd)

c Datum elevation at receiver                   SEGY_STANDARD

integer*4 delr

equivalence (thead(53),delr)

c Datum elevation at source                     SEGY_STANDARD

integer*4 dels

equivalence (thead(57),dels)

c Water depth at source                         SEGY_STANDARD

integer*4 wds

equivalence (thead(61),wds)

c Water depth at receiver                       SEGY_STANDARD

integer*4 wdr

equivalence (thead(65),wdr)

c Scalar multiplier/divisor(+/-)for bytes 41-68 SEGY_STANDARD

integer*2 smul1

equivalence (thead(69),smul1)

c Scalar multiplier/divisor(+/-)for bytes 73-88  SEGY_STANDARD

integer*2 smul2

equivalence (thead(71),smul2)

c Source coordinate X or Longitude

c (East positive)                               SEGY_STANDARD

integer*4 ishlo

equivalence (thead(73),ishlo)

c Source coordinate Y or Latitude

c (North positive)                              SEGY_STANDARD

integer*4 ishla

equivalence (thead(77),ishla)

c Group coordinate X or Longitude

c (East positive)                               SEGY_STANDARD

integer*4 irlo

equivalence (thead(81),irlo)

c Group coordinate Y or Latitude

c (North positive)                              SEGY_STANDARD

integer*4 irla

equivalence (thead(85),irla)

c Coordinate units (1 : meters/feet,           SEGY_STANDARD

c                    2 : seconds of arc

c                       (smul2 holds multiplier)

c                   -N : mod 100 = TX UTM zone

c                        div 100 = RX UTM zone

integer*2 cunits

equivalence (thead(89),cunits)

c Weathering velocity (meters(feet)/sec)        SEGY_STANDARD

integer*2 wvel

equivalence (thead(91),wvel)

c Subweathering velocity (meters(feet)/sec)     SEGY_STANDARD

integer*2 swvel

equivalence (thead(93),swvel)

c Uphole time at source                         SEGY_STANDARD

integer*2 utimes

equivalence (thead(95),utimes)

c Uphole time at group                          SEGY_STANDARD

integer*2 utimeg

equivalence (thead(97),utimeg)

c Source static correction                      SEGY_STANDARD

integer*2 sstati

equivalence (thead(99),sstati)

c Group static                                  SEGY_STANDARD

integer*2 gstati

equivalence (thead(101),gstati)

c Total static                                  SEGY_STANDARD

integer*2 tstati

equivalence (thead(103),tstati)

c Lag time A                                    SEGY_STANDARD

integer*2 istime

equivalence (thead(105),istime)

c Lag time B                                    SEGY_STANDARD

integer*2 ibtime

equivalence (thead(107),ibtime)

c Delay recording time                          SEGY_STANDARD

integer*2 ictime

equivalence (thead(109),ictime)

c The above times as defined for SEGY are not

c adequate for refraction data because they

c are limited to 32s. Use cor and tstart later on.

c Mute time start                               SEGY_STANDARD

integer*2 mtimes

equivalence (thead(111),mtimes)

c Mute time end                                 SEGY_STANDARD

integer*2 mtimee

equivalence (thead(113),mtimee)

c No of samples in this trace                   SEGY_STANDARD         R

integer*2 length

equivalence (thead(115),length)

c Sample interval in microseconds               SEGY_STANDARD         R

c See override for this value (isin, bytes 201-204) for

c more precise presentation.

integer*2 isi

equivalence (thead(117),isi)

c Gain type  (1=fixed, 2=binary, 3=floating)    SEGY_STANDARD

integer*2 gaint

equivalence (thead(119),gaint)

c Gain constant                                 SEGY_STANDARD         D

c data in nanometers/sec = (tape data)*(10**gc) SEGY_IASPEI

integer*2  gc

equivalence (thead(121),gc)

c Instrument or initial gain in dB              SEGY_STANDARD

integer*2 gidb

equivalence (thead(123),gidb)

c Correlated 1=no, 2=yes                        SEGY_STANDARD

integer*2  tcorr

equivalence (thead(125),tcorr)

c Start sweep frequency (HZ)                    SEGY_STANDARD

integer*2    tsswee

equivalence  (thead(127),tsswee)

c End sweep frequency (HZ)                      SEGY_STANDARD

integer*2    teswee

equivalence  (thead(129),teswee)

c Sweep Length in milliseconds                  SEGY_STANDARD

integer*2    tsleng

equivalence  (thead(131),tsleng)

c Sweep type                                    SEGY_STANDARD         D

c     tstype=1  linear                          SEGY_STANDARD

c     tstype=2  parabolic                       SEGY_STANDARD

c     tstype=3  exponential                     SEGY_STANDARD

c     tstype=4  other                           SEGY_STANDARD

c     tstype=5  borehole source                 SEGY_IASPEI

c     tstype=6  water explosive source          SEGY_IASPEI

c     tstype=7  airgun source                   SEGY_IASPEI

c     tstype=8  earthquake                      SEGY_IASPEI

c     tstype=9  quarry-blast                    SEGY_IASPEI

c

integer*2    tstype

equivalence  (thead(133),tstype)

c Sweep trace taper in milliseconds at start    SEGY_STANDARD

integer*2    tstts

equivalence  (thead(135),tstts)

c

c Sweep trace taper in milliseconds at end      SEGY_STANDARD

integer*2    tstte

equivalence  (thead(137),tstte)

c Taper type                                    SEGY_STANDARD

c     ttype=1 linear

c     ttype=2 cos**2

c     ttype=3 other

integer*2    tttype

equivalence  (thead(139),tttype)

c Anti alias filter frequency                   SEGY_STANDARD

integer*2    aif

equivalence  (thead(141),aif)

c Alias filter slope                            SEGY_STANDARD

integer*2    ais

equivalence  (thead(143),ais)

c Notch filter frequency                        SEGY_STANDARD

integer*2  nif

equivalence (thead(145),nif)

c Notch filter slope                            SEGY_STANDARD

integer*2    nis

equivalence  (thead(147),nis)

c Low cut frequncy                              SEGY_STANDARD

integer*2    flc

equivalence  (thead(149),flc)

c High cut frequncy                             SEGY_STANDARD

integer*2    fhc

equivalence  (thead(151),fhc)

c Low cut slope                                 SEGY_STANDARD

integer*2    slc

equivalence  (thead(153),slc)

c High cut slope                                SEGY_STANDARD

integer*2    shc

equivalence  (thead(155),shc)

c Year of start of trace                        SEGY_STANDARD         R

integer*2    tyear

equivalence  (thead(157),tyear)

c Julian day of start of trace                  SEGY_STANDARD         R

integer*2    tday

equivalence  (thead(159),tday)

c Hour of start of trace                        SEGY_STANDARD         R

integer*2    thour

equivalence  (thead(161),thour)

c Minute of start of trace                      SEGY_STANDARD         R

integer*2    tmin

equivalence  (thead(163),tmin)

c Second of start of trace                      SEGY_STANDARD         R

integer*2    tsec

equivalence  (thead(165),tsec)

c Time basis code  1=local, 2=gmt               SEGY_STANDARD         R

integer*2    tbcode

equivalence  (thead(167),tbcode)

c Trace weighting factor                        SEGY_STANDARD

integer*2    twf

equivalence  (thead(169),twf)

c Geophone group no on roll switch              SEGY_STANDARD

c first position

integer*2    ggrp1

equivalence  (thead(171),ggrp1)

c Geophone group no trace position 1 on rec     SEGY_STANDARD

integer*2    ggtp

equivalence  (thead(173),ggtp)

c Geophone group no on last trace of filed rec  SEGY_STANDARD

c     Or institution use

integer*2    gglp

equivalence  (thead(175),gglp)

c Gap size                                      SEGY_STANDARD

c     Or institution use

integer*2    gapsz

equivalence  (thead(177),gapsz)

c Field LINE number                             SEGY_IASPEI           D

integer*2    overt

equivalence  (thead(179),overt)

c Microseconds of trace start time              SEGY_IASPEI           R

integer*4   mst

equivalence (thead(181),mst)

c Charge size in kg or airgun size in litres    SEGY_IASPEI           R

integer*2   charge

equivalence (thead (185),charge)

c Shot or triger time - year                    SEGY_IASPEI           R

integer*2 syear

equivalence (thead(187),syear)

c Shot or triger time - Julian day              SEGY_IASPEI           R

integer*2 sday

equivalence (thead(189),sday)

c Shot or triger time - hour                    SEGY_IASPEI           R

integer*2 shour

equivalence (thead(191),shour)

c Shot or triger time - minute                  SEGY_IASPEI           R

integer*2 smin

equivalence (thead(193),smin)

c Shot or triger time - second                  SEGY_IASPEI           R

integer*2 sseco

equivalence (thead(195),sseco)

c Shot or triger time - microsecond             SEGY_IASPEI           R

integer*4 ssmic

equivalence (thead(197),ssmic)

c Override for sample interval.                 SEGY_IASPEI           D

c This variable is related to variable isi bytes (117-118).

c If this variable is set to non-zero, it holds a more

c precise value than isi.

c

c This is the status table for the value of this variable:

c      Variable Name  Overrides  Value       Result

c      isin           isi        0           No action

c      isin           isi        < 0         Sample rate in samples per second

c      isin           isi        > 0         Sample interval in Nanoseconds

c

integer*4 isin

equivalence (thead(201),isin)

c Azimuth of geophone orientation axis with     SEGY_IASPEI           D

c respect to true north in minutes of arc

integer*2 geoazi

equivalence (thead(205),geoazi)

c Angle between geophone orientation axis and   SEGY_IASPEI           D

c vertical in minutes of arc

integer*2 geover

equivalence (thead(207),geover)

c Static correction                             SEGY_IASPEI           D

c time to be added to recorded trace time to

c get actual trace start

c time. To be used when data has been reduced

integer*4   ttrace

equivalence (thead (209),ttrace)

c Flag to signal that ttrace has been used to   SEGY_IASPEI           D

c modify trace start time

c  tapply=0   static ttrace has been used to

c             reduce the data

c             and trace start time updated

c  tapply=1   static ttrace has beed has been

c             used to reduce the data but trace

c             start time has not been corrected

c

integer*2   tapply

equivalence (thead(213),tapply)

c Recording instrument type                     SEGY_IASPEI           R

c If instrument types in reel header and trace

c header are different, then the trace header value

c must be used.

c

c       =0 Not specified.

c       =1 EDA (Scintrex) PRS1

c       =2 USGS cassette

c       =3 GEOS

c       =4 Springnether

c       =5 Teledyne

c       =6 Kinemetrics

c       =7 SGR

c       =8 TERATEK

c       =9 EDA (Scintrex) PRS4

c       =10 MARS 88

c       =11 MARS 66

c       =12 PCM 5800

c       =13 REFTEK

c       =14 GEOSTORE

integer*2 instru

equivalence(thead(215),instru)

c Millisecond of timing correction              SEGY_IASPEI           R

c to be added to reported times to get true

c local or gmt times.

c This should be the sum of all timing

c corrections such as master clock and

c seismograph drifts.

integer*2   cor

equivalence (thead(217),cor)

c Azimuth of receiver                           SEGY_IASPEI           D

c from shot in minutes of arc

integer*2 azimut

equivalence (thead(219),azimut)

c

c---------------------------------------------------------------------+

c Binary part of Trace Identification Header Ends here                |

c---------------------------------------------------------------------+

c Character information.

c Recording instrument name

character*4   scrs

equivalence (thead (221),scrs)

c Shotpoint name

character*4 spname

equivalence (thead(225),spname)

c Receiver site name

character*4 rstnam

equivalence (thead(229),rstnam)

c Shot site name

character*4 shotid

equivalence (thead(233),shotid)

c Geophone mnemonic

c for example L4-Z, L4-N

c use reel header to explain the mnemonics

c used on a tape.

character*4 geopin

equivalence (thead (237),geopin)

c

c---------------------------------------------------------------------+

c Trace Identification Header (total of 240 bytes) Ends   here        |

c---------------------------------------------------------------------+

c

c- End   of FINAL segy.inc version 3.00 (IASPEI), January 25, 1993 ----