## Slide 1: The iLoc Locator: Tutorial
István Bondár
Research Centre for Astronomy and Earth Sciences, Hungarian Academy of Sciences
Training in Network Management Systems and Analytical Tools for Seismology
Baku, Azerbaijan, 23-27 October 2017

## Slide 2: How to run iLoc
Set the environment variables
Check if all iLoc data files are up-to-date
Familiarize with the configuration parameters
Edit the config.txt file, if necessary
Familiarize with the command line parameters
Read the Manual
Play with the locator
Inspect the log file (always recommended)
Do several trial and error runs to find the optimal configuration parameters

## Slide 3: Set environment variables
ILOCROOT
Directory pathname for iLoc data files (TT tables, etc).
SLBMROOT
Directory pathname for the RSTT root directory.
Example .bashrc excerpt:
#
# RSTT, iLoc
#
export SLBMROOT=~/SLBM_Root.3.0.5.Linux
export ILOCROOT=~/iLocRelease1.60
export PATH=$PATH:~/bin
export LD_LIBRARY_PATH=/usr/lib:/usr/local/lib:$SLBMROOT/lib

## Slide 4: iLoc data files

## Slide 5: Configuration parameters
$ILOCROOT/etc/iLocpars/config.txt
  General parameters that control the behaviour of the locator
$ILOCROOT/etc/iLocpars/ak135_model.txt
  Phase-specific pars, such as phase name mappings to IASPEI phase names, a priori measurement errors, etc.
See Tables 4 and 5 in the Manual for detailed lists of parameters
Most commonly used config pars can also be set in the command line instructions
Do not forget to set the full pathnames of the isf_stafile and rstt_model parameters in the config.txt file!

## Slide 6: Running the locator
ISF/ISF2 text file input:
echo “isf_infile=ISF_input_file [instructions]” | iloc isf
echo “isf_infile=ISF2_input_file [instructions]” | iloc isf2
echo ”isf_infile=myin.isf isf_outfile=myout.isf2" | iloc isf2 > my.log
SeisComp3 DB interface:
echo “eventid [instructions]” | iloc_sc3db sc3db
iloc_sc3db sc3db < instruction_file > log_file
echo ”bud2015colr use_RSTT_PnSn=1" | iloc_sc3db sc3db > bud2015colr.log
iloc_sc3db sc3db < myinstructions.txt > myiloc.log

## Slide 7: Command line instructions
Instructions control the behaviour of the locator
  Features can be turned on and off
  Default configuration parameters can be overridden
  Initial guess for any hypocentre parameters can be provided
  Any hypocentre parameters can be fixed
For ISF/ISF2 input only the first line of the instruction file is interpreted, and the instructions are applied to all events in the input ISF/ISF2 file.
If you want to have individual instructions for each event, you have to put the events in different ISF files.

## Slide 8: Instructions
ISF input/output files
isf_infile Full pathname to the ISF/ISF2 input text file.
isf_outfile Full pathname to the ISF/ISF2 output text file.
isf_stafile Full pathname to the station file.
Use isc_stalist for ISF files and IR2_stalist for ISF2 files!
RSTT-specific parameters
rstt_model Full pathname to the RSTT model.
use_RSTT_PnSn Use RSTT mantle phase predictions or not [0/1].
use_RSTT_PgLg Use RSTT crustal phase predictions or not [0/1].
Local velocity model
localvmodel Full pathname to the local velocity model.
max_localTT_delta Local TT used up to this distance. Default is 3 degrees.
Account for correlated errors
do_correlated_errors Set it to 0 to turn it off [0/1]. Always enable it!

## Slide 9: Instructions, cont’d
Initial hypocenter parameters
lat A latitude value or an agency code to start the locator from.
lon A longitude value or an agency code to start the locator from.
depth A depth value or an agency code to start the locator from.
time An origin time (YYYY-MM-DD_HH:MM:SS.SSS) value or an agency code to start the locator from.
Fix hypocenter parameters
fix_hypo An agency code to fix the hypocentre to. If no code is given, the hypocentre will be fixed to the median reported hypocentre (lat, lon, depth and origin time) parameters.
fix_location An agency code to fix the epicentre to.
fix_depth A depth value or an agency code to fix the depth to.
fix_time An origin time (YYYY-MM-DD_HH:MM:SS.SSS) value or an agency code to fix the origin time to.

## Slide 10: Instructions, cont’d
Perform nearest neighbor search to get initial hypocenter
do_gridsearch Set it to 1 to turn it on [0/1].
Grid search parameters
na_radius Search radius around starting epicentre (degrees).
na_deptol Search radius around starting depth (km).
na_ottol Search radius around starting origin time (s).
na_nsamplei Number of initial samples in NA search.
na_nsample Number of subsequent samples in NA search.
na_cells Number of cells to be resampled in NA search.
write_gridsearch_results Write Neighbourhood Algorithm results to file [0/1].

## Slide 11: Instructions, cont’d
Depth resolution criteria
mindepthpha Minimum number of time-defining first arriving P and depth phase pairs for depth-phase depth resolution.
mincorepha Minimum number of time-defining first arriving P and core phase (PcP, ScS) pairs for depth resolution.
localdist Maximum epicentral distance for local stations (degrees).
minlocalsta Minimum number of time-defining first arriving P within localdist for depth resolution.
spdist Maximum epicentral distance for near-regional stations (degrees).
min_s_p Minimum number of time-defining first arriving P and S pairs within spdist for depth resolution.

## Slide 12: iLoc logfile
Contains useful information not found in ISF output file
Initial guess
NA search results
Depth resolution
Station magnitudes
Phase lines with velocity model used
Final solution
GT candidate test
Verbosity level can be set in the instruction line
Verbose: 0-6 with increasing verbosity
It is always recommended to look at the logfile

## Slide 13: iLoc logfile: Instructions
Event: 2006/02/06 04:08:01, 42.564, 43.5157, 14.85, 5.2 mb
First line shows the iLoc instructions
Instruction: echo "isf_infile=20060206040801.isf do_gridsearch=1 use_RSTT_PnSn=0 use_RSTT_PgLg=0" | iloc isf
Instruction: echo "isf_infile=20060206040801.isf do_gridsearch=1 use_RSTT_PnSn=1 use_RSTT_PgLg=1" | iloc isf

## Slide 14: iLoc logfile: Initial hypocentre
if there is a IASPEI hypo, it takes precedence, otherwise the initial guess will be the median of reported hypocentre parameters
numhyps=13 numphas=1427
hypid agency time lat lon depth nsta sdef ndef nass gap mindist stime sdep smaj
9824665 ISC 2006-02-06 04:08:03.950 42.650 43.499 23.5 0 808 904 0 8.0 0.08 0.09 1.8
11249093 EHB 2006-02-06 04:08:03.210 42.615 43.485 17.7 0 784 897 0 1.30 2.1
8934672 ISC-EHB 2006-02-06 04:08:03.140 42.618 43.495 17.0 0 619 675 0 1.30 26.0
7849731 HRVD 2006-02-06 04:08:03.100 42.650 43.450 14.0 0 94 306 0 0.20 2.2
9815096 NEIC 2006-02-06 04:08:03.070 42.653 43.525 17.0 0 320 0 40.0 1.44 1.27 8.30 3.4
8883182 TIF 2006-02-06 04:08:01.320 42.550 43.454 10.3 0 53 0 63.0 0.04 1.70
9809336 MOS 2006-02-06 04:08:00.700 42.650 43.459 11.0 0 253 0 1.14 3.5
8217612 IDC 2006-02-06 04:07:59.800 42.559 43.594 0.0 0 58 0 47.0 2.56 0.32 8.2
7101113 CSEM 2006-02-06 04:07:59.700 42.600 43.570 10.0 0
Median hypocentre:
OT = 2006-02-06 04:08:03.070 Lat = 42.623 Lon = 43.485 Depth = 17.0
Option 0
Initial hypocentre:
OT = 2006-02-06 04:08:03.070 Lat = 42.623 Lon = 43.485 Depth = 17.0

## Slide 15: iLoc logfile: Grid search results
Phases are reidentified w.r.t. the initial guess for the hypocentre
Neighbourhood Algorithm grid search (if any) to get a refined initial guess for the hypocentre
Neighbourhood algorithm (0.0467)
Best fitting hypocentre from grid search:
OT = 2006-02-06 04:08:03.070 Lat = 42.623 Lon = 43.485 Depth = 17.0
Distance from initial guess = 0.0 km
Reidentify phases after NA
NA (28.2177) done
Phases are reidentified w.r.t. the NA hypocentre

## Slide 16: iLoc logfile: Depth resolution test
Depth resolution for free-depth solution
Depth-phase depth resolution: 1
1 agencies reported 72 defining depth phases
Depth resolution: 1
1 stations within 0.20 degrees
19 defining S-P pairs within 2.00 degrees
1 agencies reported 16 defining PcP/ScS phases
If there is no depth resolution, depth is fixed to the corresponding value in the default depth grid
Depth-phase depth resolution: 0
0 agencies reported 0 defining depth phases
Depth resolution: 0
0 stations within 0.20 degrees
0 defining S-P pairs within 3.00 degrees
0 agencies reported 0 defining PcP/ScS phases
No depth resolution for free-depth solution!
Fix depth by default depth grid: 10.00

## Slide 17: iLoc logfile: Location
Event location
Event location
convergent solution after 5 iterations
Convergent solution, final touches
If there is depth-phase depth resolution w.r.t. the final solution, depth-phase stack is performed
Depth-phase depth resolution: 1
1 agencies reported 72 defining depth phases
ndp = 62, depth=17.0, depth error=3.9

## Slide 18: iLoc logfile: Station magnitudes
Station magnitudes (at least 3 defining station magnitude is required to calculate network magnitude)
iLoc calculates mb, MS, ML and mB
200 mb station magnitudes
…
GERES stamag=4.937 magdef=0
SUMG stamag=4.938 magdef=1
…
agencies contributing to mb
1 FDSN 201 readings
59 MS station magnitudes
TREC stamag=4.684 magdef=0
BOSA stamag=4.739 magdef=1
…
agencies contributing to MS
1 FDSN 59 readings
9 ML station magnitudes
BRTR stamag=4.382 magdef=0
ANN stamag=4.780 magdef=1
…
33 mB station magnitudes
MORC stamag=5.731 magdef=0
KK31 stamag=5.756 magdef=1

## Slide 19: iLoc logfile: Phases
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 16641870 FDSN.IR.ONI.-- ??? Pb Pg 1 2006-02-06 04:08:03.861 0.02 229.46 0.800 10 -1.642 ak135
1 16641871 FDSN.IR.ONI.-- ??? Sb Lg 0 2006-02-06 04:08:05.679 0.02 229.46 1.500 10 -1.668 ak135
2 22525861 FDSN.IR.DIGR.-- ??? Pb Pg 1 2006-02-06 04:08:08.600 0.30 14.53 0.800 10 -0.481 ak135
2 22525862 FDSN.IR.DIGR.-- ??? Sb Sg 0 2006-02-06 04:08:13.900 0.30 14.53 1.500 10 0.285 ak135
3 22526059 FDSN.IR.ZEI.-- ??? Pb Pg 1 2006-02-06 04:08:09.200 0.36 59.65 0.800 10 -0.872 ak135
3 22526060 FDSN.IR.ZEI.-- ??? Sb Lg 0 2006-02-06 04:08:14.900 0.36 59.65 1.500 10 -0.151 ak135
4 22525934 FDSN.IR.LACR.-- ??? Pb Pg 1 2006-02-06 04:08:14.300 0.64 69.63 0.800 10 -0.864 ak135
4 22525935 FDSN.IR.LACR.-- ??? Sb Lg 0 2006-02-06 04:08:23.800 0.64 69.63 1.500 10 0.119 ak135
5 22525938 FDSN.IR.LSNR.-- ??? Pb Pg 1 2006-02-06 04:08:16.200 0.72 20.75 0.800 10 -0.353 ak135
5 22525939 FDSN.IR.LSNR.-- ??? Sb Sb 0 2006-02-06 04:08:26.900 0.72 20.75 1.500 10 0.696 ak135
7 22604143 FDSN.IR.GOR.-- ??? Pb Pn 1 2006-02-06 04:08:25.000 0.78 142.71 0.800 00 6.293 ak135
7 16641858 FDSN.IR.GOR.-- ??? Pb Pg 0 2006-02-06 04:08:35.307 0.78 142.71 0.800 00 17.684 ak135
7 16641859 FDSN.IR.GOR.-- ??? Sb Sn 0 2006-02-06 04:08:46.934 0.78 142.71 1.500 00 16.926 ak135
6 22525819 FDSN.IR.ARNR.-- ??? Pb Pb 1 2006-02-06 04:08:18.100 0.83 45.66 0.800 10 -0.269 ak135
6 22525820 FDSN.IR.ARNR.-- ??? Sb Sg 0 2006-02-06 04:08:30.400 0.83 45.66 1.500 10 0.952 ak135
8 22526034 FDSN.IR.VLKR.-- ??? Pb Pb 1 2006-02-06 04:08:20.900 0.99 63.09 0.800 10 -0.237 ak135
8 22526035 FDSN.IR.VLKR.-- ??? Sb Sg 0 2006-02-06 04:08:35.100 0.99 63.09 1.500 10 0.548 ak135
9 16641868 FDSN.IR.CHVG.-- ??? Pn Pb 1 2006-02-06 04:08:21.161 1.03 276.71 0.800 10 -0.751 ak135
9 16641869 FDSN.IR.CHVG.-- ??? Sb Sb 0 2006-02-06 04:08:35.806 1.03 276.71 1.500 10 0.602 ak135
10 16641866 FDSN.IR.DUS.-- ??? Pn Pb 1 2006-02-06 04:08:21.414 1.04 119.17 0.800 10 -0.712 ak135
10 16641867 FDSN.IR.DUS.-- ??? Sb Sb 0 2006-02-06 04:08:36.490 1.04 119.17 1.500 10 0.930 ak135
...
112 22604244 FDSN.IR.VAN.-- ??? Pn Pn 1 2006-02-06 04:10:52.900 12.10 107.73 0.800 10 -1.223 ak135
113 09649640 FDSN.IR.ABKT.-- ??? Pn Pn 1 2006-02-06 04:10:52.900 12.12 107.78 0.800 10 -1.449 702.7 ??? 0 ak135
114 00640762 FDSN.IR.EDRB.-- ??? Pn Pn 1 2006-02-06 04:10:57.300 12.43 272.16 0.800 10 -1.268 ak135
115 22892835 FDSN.IR.VRI.-- ??? Pn P 1 2006-02-06 04:11:07.295 12.45 290.89 0.800 10 -3.321 ak135
118 11849352 FDSN.IR.AKASG.-- ??? Pn Pn 1 2006-02-06 04:11:00.550 12.69 314.54 0.800 10 -1.476 3.1 ??? 0 ak135
118 22525810 FDSN.IR.AKASG.-- ??? Pn P 0 2006-02-06 04:11:00.600 12.69 314.54 0.800 00 -12.628 ak135
118 22892437 FDSN.IR.AKASG.-- ??? Sn Sn 0 2006-02-06 04:13:18.673 12.69 314.54 1.500 10 -4.131 ak135
118 11849354 FDSN.IR.AKASG.-- ??? Lg 0 2006-02-06 04:14:47.050 12.69 314.54 00 ak135
119 22525921 FDSN.IR.KIEV.-- ??? Pn Pn 1 2006-02-06 04:11:02.000 12.69 314.49 0.800 10 -0.084 ak135
116 22525812 FDSN.IR.AKTK.-- ??? Pn Pn 1 2006-02-06 04:10:59.500 12.69 46.93 0.800 10 -2.633 ak135
116 22892439 FDSN.IR.AKTK.-- ??? Pn P 0 2006-02-06 04:10:59.530 12.69 46.93 0.800 00 -13.795 ak135
116 22525813 FDSN.IR.AKTK.-- ??? Sn Sn 0 2006-02-06 04:13:15.200 12.69 46.93 1.500 10 -7.789 ak135
...
570 11849418 FDSN.IR.PDAR.-- ??? P P 1 2006-02-06 04:21:08.550 91.62 340.49 0.800 10 -0.240 mb 1.9 0.9 ??? 1 ak135
570 11849419 FDSN.IR.PDAR.-- ??? LR LR 0 2006-02-06 05:03:50.170 91.62 340.49 00 MS 605.3 18.4 ??? 1 null
571 22892738 FDSN.IR.PHWY.-- ??? P P 1 2006-02-06 04:21:10.910 91.89 337.11 0.800 10 0.757 ak135
571 22892739 FDSN.IR.PHWY.-- ??? pP sP 0 2006-02-06 04:21:18.440 91.89 337.11 1.300 10 0.022 ak135
572 22892612 FDSN.IR.ISCO.-- ??? P P 1 2006-02-06 04:21:17.395 93.32 336.65 0.800 10 0.584 mb 14.5 1.4 ??? 1 ak135
572 22604693 FDSN.IR.ISCO.-- ??? pP pP 0 2006-02-06 04:21:24.010 93.32 336.65 1.300 10 1.124 ak135
572 22604692 FDSN.IR.ISCO.-- ??? pmax pmax 0 93.32 336.65 00 mb 14.0 1.4 ??? 0 null
573 22892696 FDSN.IR.MOD.-- ??? P P 1 2006-02-06 04:21:23.690 94.61 347.92 0.800 10 1.200 mb 11.4 1.1 ??? 1 ak135
573 22892697 FDSN.IR.MOD.-- ??? pP sP 0 2006-02-06 04:21:31.080 94.61 347.92 1.300 10 0.333 ak135
574 11849372 FDSN.IR.ELK.-- ??? P P 1 2006-02-06 04:21:25.375 94.83 343.93 0.800 10 1.767 mb 2.4 0.8 ??? 1 ak135
575 11849416 FDSN.IR.NVAR.-- ??? P P 1 2006-02-06 04:21:36.050 97.66 345.65 0.800 10 -0.439 mb 0.2 0.6 ??? 1 ak135
576 22604695 FDSN.IR.ANMO.-- ??? P Pdif 1 2006-02-06 04:21:39.100 98.06 335.44 00 0.719 ak135
577 11849429 FDSN.IR.TXAR.-- ??? Pdif Pdif 1 2006-02-06 04:21:56.550 102.29 331.00 2.800 10 -0.579 0.3 ??? 0 ak135
578 11849436 FDSN.IR.WRA.-- ??? PP PP 1 2006-02-06 04:26:25.809 103.84 104.36 0.000 00 4.539 1.0 ??? 0 ak135
579 11849404 FDSN.IR.LVC.-- ??? PKPdf PKPdf 1 2006-02-06 04:26:55.110 121.18 267.00 1.300 10 0.144 2.2 ??? 0 ak135
580 11849420 FDSN.IR.PLCA.-- ??? PKPdf PKPdf 1 2006-02-06 04:27:14.150 131.83 248.66 1.300 10 -0.255 4.3 ??? 0 ak135
581 11849433 FDSN.IR.USHA.-- ??? PKPdf PKPdf 1 2006-02-06 04:27:19.437 135.20 229.62 1.300 10 -0.675 4.9 ??? 0 ak135
582 11849351 FDSN.IR.AFI.-- ??? PKPdf PKPdf 1 2006-02-06 04:27:25.310 138.29 57.40 1.300 10 -1.892 18.8 ??? 0 ak135
583 11849432 FDSN.IR.URZ.-- ??? PKPdf PKPab 1 2006-02-06 04:27:35.156 144.78 98.87 1.300 10 -1.853 29.4 ??? 0 ak135

## Slide 20: iLoc logfile: Phases
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 16641870 FDSN.IR.ONI.-- ??? Pb Pg 1 2006-02-06 04:08:03.861 0.04 6.29 0.800 10 -1.483 RSTT
1 16641871 FDSN.IR.ONI.-- ??? Sb Lg 0 2006-02-06 04:08:05.679 0.04 6.29 1.500 10 -2.003 RSTT
2 22525861 FDSN.IR.DIGR.-- ??? Pb Pg 1 2006-02-06 04:08:08.600 0.36 15.77 0.800 10 -1.542 RSTT
2 22525862 FDSN.IR.DIGR.-- ??? Sb Lg 0 2006-02-06 04:08:13.900 0.36 15.77 1.500 10 -2.304 RSTT
3 22526059 FDSN.IR.ZEI.-- ??? Pb Pg 1 2006-02-06 04:08:09.200 0.41 54.50 0.800 10 -1.837 RSTT
3 22526060 FDSN.IR.ZEI.-- ??? Sb Lg 0 2006-02-06 04:08:14.900 0.41 54.50 1.500 10 -2.873 RSTT
4 22525934 FDSN.IR.LACR.-- ??? Pb Pg 1 2006-02-06 04:08:14.300 0.69 65.89 0.800 10 -1.443 RSTT
4 22525935 FDSN.IR.LACR.-- ??? Sb Lg 0 2006-02-06 04:08:23.800 0.69 65.89 1.500 10 -2.010 RSTT
7 22604143 FDSN.IR.GOR.-- ??? Pb Pg 1 2006-02-06 04:08:25.000 0.75 138.71 0.800 00 8.146 RSTT
7 16641858 FDSN.IR.GOR.-- ??? Pb Pb 0 2006-02-06 04:08:35.307 0.75 138.71 0.800 00 18.453 RSTT
7 16641859 FDSN.IR.GOR.-- ??? Sb Lg 0 2006-02-06 04:08:46.934 0.75 138.71 1.500 00 19.237 RSTT
5 22525938 FDSN.IR.LSNR.-- ??? Pb Pg 1 2006-02-06 04:08:16.200 0.78 20.84 0.800 10 -1.028 RSTT
5 22525939 FDSN.IR.LSNR.-- ??? Sb Lg 0 2006-02-06 04:08:26.900 0.78 20.84 1.500 10 -1.326 RSTT
6 22525819 FDSN.IR.ARNR.-- ??? Pb Pg 1 2006-02-06 04:08:18.100 0.88 44.08 0.800 10 -0.963 RSTT
6 22525820 FDSN.IR.ARNR.-- ??? Sb Lg 0 2006-02-06 04:08:30.400 0.88 44.08 1.500 10 -1.044 RSTT
9 16641868 FDSN.IR.CHVG.-- ??? Pn Pg 1 2006-02-06 04:08:21.161 1.02 279.96 0.800 10 -1.378 RSTT
9 16641869 FDSN.IR.CHVG.-- ??? Sb Lg 0 2006-02-06 04:08:35.806 1.02 279.96 1.500 10 -1.699 RSTT
8 22526034 FDSN.IR.VLKR.-- ??? Pb Pg 1 2006-02-06 04:08:20.900 1.03 60.87 0.800 10 -1.087 RSTT
8 22526035 FDSN.IR.VLKR.-- ??? Sb Lg 0 2006-02-06 04:08:35.100 1.03 60.87 1.500 10 -1.584 RSTT
10 16641866 FDSN.IR.DUS.-- ??? Pn Pg 1 2006-02-06 04:08:21.414 1.04 115.84 0.800 10 -0.980 RSTT
10 16641867 FDSN.IR.DUS.-- ??? Sb Lg 0 2006-02-06 04:08:36.490 1.04 115.84 1.500 10 -0.728 RSTT
...
112 22604244 FDSN.IR.VAN.-- ??? Pn Pn 1 2006-02-06 04:10:52.900 12.11 107.42 0.800 10 -0.226 RSTT
113 09649640 FDSN.IR.ABKT.-- ??? Pn Pn 1 2006-02-06 04:10:52.900 12.12 107.48 0.800 10 -0.465 702.7 ??? 0 RSTT
114 00640762 FDSN.IR.EDRB.-- ??? Pn Pn 1 2006-02-06 04:10:57.300 12.41 272.39 0.800 10 -1.052 RSTT
115 22892835 FDSN.IR.VRI.-- ??? Pn P 1 2006-02-06 04:11:07.295 12.45 291.14 0.800 10 -3.199 ak135
118 11849352 FDSN.IR.AKASG.-- ??? Pn Pn 1 2006-02-06 04:11:00.550 12.71 314.77 0.800 10 -1.099 3.1 ??? 0 RSTT
118 22525810 FDSN.IR.AKASG.-- ??? Pn P 0 2006-02-06 04:11:00.600 12.71 314.77 0.800 00 -12.777 ak135
118 22892437 FDSN.IR.AKASG.-- ??? Sn Sn 0 2006-02-06 04:13:18.673 12.71 314.77 1.500 10 -3.896 RSTT
118 11849354 FDSN.IR.AKASG.-- ??? Lg Lg 0 2006-02-06 04:14:47.050 12.71 314.77 00 9.561 RSTT
119 22525921 FDSN.IR.KIEV.-- ??? Pn Pn 1 2006-02-06 04:11:02.000 12.72 314.72 0.800 10 0.309 RSTT
116 22525812 FDSN.IR.AKTK.-- ??? Pn Pn 1 2006-02-06 04:10:59.500 12.75 46.80 0.800 10 -1.636 RSTT
116 22892439 FDSN.IR.AKTK.-- ??? Pn P 0 2006-02-06 04:10:59.530 12.75 46.80 0.800 00 -14.297 ak135
116 22525813 FDSN.IR.AKTK.-- ??? Sn Sn 0 2006-02-06 04:13:15.200 12.75 46.80 1.500 10 -0.324 RSTT
...
570 11849418 FDSN.IR.PDAR.-- ??? P P 1 2006-02-06 04:21:08.550 91.66 340.46 0.800 10 -0.353 mb 1.9 0.9 ??? 1 ak135
570 11849419 FDSN.IR.PDAR.-- ??? LR LR 0 2006-02-06 05:03:50.170 91.66 340.46 00 MS 605.3 18.4 ??? 1 null
571 22892738 FDSN.IR.PHWY.-- ??? P P 1 2006-02-06 04:21:10.910 91.93 337.09 0.800 10 0.655 ak135
571 22892739 FDSN.IR.PHWY.-- ??? pP sP 0 2006-02-06 04:21:18.440 91.93 337.09 1.300 10 -0.040 ak135
572 22892612 FDSN.IR.ISCO.-- ??? P P 1 2006-02-06 04:21:17.395 93.37 336.62 0.800 10 0.485 mb 14.5 1.4 ??? 1 ak135
572 22604693 FDSN.IR.ISCO.-- ??? pP pP 0 2006-02-06 04:21:24.010 93.37 336.62 1.300 10 1.018 ak135
572 22604692 FDSN.IR.ISCO.-- ??? pmax pmax 0 93.37 336.62 00 mb 14.0 1.4 ??? 0 null
573 22892696 FDSN.IR.MOD.-- ??? P P 1 2006-02-06 04:21:23.690 94.66 347.90 0.800 10 1.066 mb 11.4 1.1 ??? 1 ak135
573 22892697 FDSN.IR.MOD.-- ??? pP sP 0 2006-02-06 04:21:31.080 94.66 347.90 1.300 10 0.222 ak135
574 11849372 FDSN.IR.ELK.-- ??? P P 1 2006-02-06 04:21:25.375 94.87 343.91 0.800 10 1.645 mb 2.4 0.8 ??? 1 ak135
575 11849416 FDSN.IR.NVAR.-- ??? P P 1 2006-02-06 04:21:36.050 97.71 345.63 0.800 10 -0.562 mb 0.2 0.6 ??? 1 ak135
576 22604695 FDSN.IR.ANMO.-- ??? P Pdif 1 2006-02-06 04:21:39.100 98.11 335.41 00 0.630 ak135
577 11849429 FDSN.IR.TXAR.-- ??? Pdif Pdif 1 2006-02-06 04:21:56.550 102.32 330.97 2.800 10 -0.652 0.3 ??? 0 ak135
578 11849436 FDSN.IR.WRA.-- ??? PP PP 1 2006-02-06 04:26:25.809 103.84 104.35 0.000 00 4.576 1.0 ??? 0 ak135
579 11849404 FDSN.IR.LVC.-- ??? PKPdf PKPdf 1 2006-02-06 04:26:55.110 121.15 266.94 1.300 10 0.287 2.2 ??? 0 ak135
580 11849420 FDSN.IR.PLCA.-- ??? PKPdf PKPdf 1 2006-02-06 04:27:14.150 131.78 248.60 1.300 10 -0.082 4.3 ??? 0 ak135
581 11849433 FDSN.IR.USHA.-- ??? PKPdf PKPdf 1 2006-02-06 04:27:19.437 135.14 229.57 1.300 10 -0.481 4.9 ??? 0 ak135
582 11849351 FDSN.IR.AFI.-- ??? PKPdf PKPdf 1 2006-02-06 04:27:25.310 138.34 57.42 1.300 10 -1.889 18.8 ??? 0 ak135
583 11849432 FDSN.IR.URZ.-- ??? PKPdf PKPab 1 2006-02-06 04:27:35.156 144.80 98.93 1.300 10 -1.809 29.4 ??? 0 ak135

## Slide 21: iLoc logfile: Solution
ak135
final : Western Caucasus
OT = 2006-02-06 04:08:02.493 Lat = 42.606 Lon = 43.477 Depth = 17.0
etype=fe nreading=583 nass=1427 ndef=959 ndefsta=553 nrank=587 sdobs=2.003 sgap= 11.3
smajax=2.7 sminax=2.3 strike=20.6 stime=0.227 sdepth=1.2
depdp=17.00 +/- 3.86 ndp=62
free-depth solution
local network: nsta=16 ndef=33 sgap=103.4 dU=0.328 ndefsta_10km=1 GT5cand=1
mb=5.34 +/- 0.22 nsta=200
MS=4.93 +/- 0.21 nsta=59
ML=5.47 +/- 1.02 nsta=9
mB=6.40 +/- 0.24 nsta=33
Finished event 8079912 (30.13)
EVENT 30.133472 1427
RSTT
final : Western Caucasus
OT = 2006-02-06 04:08:02.317 Lat = 42.550 Lon = 43.446 Depth = 16.5
etype=fe nreading=583 nass=1427 ndef=955 ndefsta=550 nrank=580 sdobs=1.993 sgap= 13.1
smajax=2.6 sminax=2.4 strike=38.3 stime=0.227 sdepth=1.2
depdp=17.00 +/- 4.58 ndp=61
free-depth solution
local network: nsta=16 ndef=33 sgap=156.5 dU=0.418 ndefsta_10km=1 GT5cand=0
mb=5.34 +/- 0.21 nsta=201
MS=4.93 +/- 0.21 nsta=59
ML=5.49 +/- 1.05 nsta=9
mB=6.41 +/- 0.23 nsta=32
Finished event 8079912 (284.39)
EVENT 284.393618 1427

## Slide 22: RSTT and ak135 solutions are 6 km apart
ak135
RSTT

## Slide 23: Using RSTT
RSTT Pn, Sn and Pg, Lg prediction can be turned on and off separately (config.txt or instruction)
use_RSTT_PnSn = 1 # use RSTT PnSn predictions?
use_RSTT_PgLg = 0 # use RSTT Pg/Lg predictions?
You can specify your own RSTT model (config.txt)
rstt_model=/Users/istvan/CostaRica/rstt201404um.geotess

## Slide 24: Using a local velocity model
Local velocity model can be specified (config.txt)
localvmodelfile = full pathname for the local velocity model
Format for the 1D velocity model
#
# ak135
#
# number of layers
4
0.000 5.8000 3.4600 x
20.000 6.5000 3.8500 CONRAD
35.000 8.0400 4.4800 MOHO
77.500 8.0400 4.4800 x

## Slide 25: Exercises: examine the input data
Locate event 2017/07/07, Eastern Caucasus
There is no ISC solution yet, but most data are already at ISC
Recent event, not all agencies reported it yet
Local/regional: TIF and NSSP
Global: NEIC, IDC, GFZ, MOS, BJI
DATA_TYPE BULLETIN IMS1.0:short
ISC Bulletin
Event 610666945 Eastern Caucasus
Date Time Err RMS Latitude Longitude Smaj Smin Az Depth Err Ndef Nsta Gap mdist Mdist Qual Author OrigID
2017/06/07 18:25:39.00 0.00 1.380 41.4000 45.8000 10.0 54 320 22.80 59.40 uk BJI 09071424
2017/06/07 18:25:40.80 41.4600 45.7300 10.0 20 MOS 08550849
2017/06/07 18:25:41 41.4580 45.9220 10.0 NEIC 08550868
2017/06/07 18:25:41.80 41.6100 46.0500 10.0 72 GFZ 08550837
2017/06/07 18:25:41.80 0.350 41.4056 45.7956 29.4 1.1 84 20 0.47 TIF 08895762
2017/06/07 18:25:42.80 41.3667 45.7167 12.0 NSSP 08907501
2017/06/07 18:25:38.90 0.48 0.950 41.3974 45.8021 7.4 6.8 7 0.0f 42 68 1.48 75.26 uk IDC 08901563
(#PRIME)

## Slide 26: Exercises

## Slide 27: Exercises
Reported magnitudes
Magnitude Err Nsta Author OrigID
mb 4.8 48 BJI 09071424
mB 4.8 21 BJI 09071424
Ms 4.2 13 BJI 09071424
Ms7 3.9 13 BJI 09071424
MB 4.8 MOS 08550849
4.7 NEIC 08550868
mb 4.5 72 GFZ 08550837
Ms 4.9 NSSP 08907501
mb 4.2 0.1 22 IDC 08901563
mbtmp 4.3 0.1 32 IDC 08901563
ML 3.8 0.2 9 IDC 08901563
MS 3.7 0.0 49 IDC 08901563

## Slide 28: Exercises
Reported phases (ordered by sta, dist; no calculated residuals)
Sta Dist EvAz Phase Time TRes Azim AzRes Slow SRes Def SNR Amp Per Qual Magnitude ArrID
DDFL 0.24 78.4 Pg 18:25:51.3 7.8 ___ __ 87629787
DDFL 0.24 78.4 S 18:25:58.76 ___ __ 87629788
LGD 0.55 36.9 Pn 18:25:53.31 0.7 ___ __ 87629793
LGD 0.55 36.9 S 18:26:02.01 ___ __ 87629794
SEAG 0.83 296.4 Pn 18:25:57.89 0.1 ___ __ 87629801
SEAG 0.83 296.4 S 18:26:09.92 ___ __ 87629802
KZRT 1.06 269.9 Pb 18:26:00.46 0.4 ___ __ 87629791
KZRT 1.06 269.9 S 18:26:14.52 ___ __ 87629792
STE 1.15 250.3 P 18:26:02.18 ___ ci 87861232
STE 1.15 250.3 S 18:26:17.31 ___ ci 87861233
KMKR 1.22 52.5 P 18:26:04.3 ___ ci 85738126
TRLG 1.29 276.9 Pb 18:26:04.06 0.0 ___ __ 87629807
TRLG 1.29 276.9 S 18:26:21 ___ __ 87629808
BTLR 1.30 13.8 P 18:26:06.2 ___ _i 85738127
SHTL 1.35 339.2 Pb 18:26:06.24 1.1 ___ __ 87629803
SHTL 1.35 339.2 S 18:26:23.88 ___ __ 87629804
KAPZ 1.36 218.3 P 18:26:06.49 ___ ci 87861244
KAPZ 1.36 218.3 S 18:26:25.01 ___ di 87861245
AKT 1.45 86.1 P 18:26:07.5 ___ _i 85738128
GUDG 1.45 317.6 Pb 18:26:08.16 1.2 ___ __ 87629789
GUDG 1.45 317.6 S 18:26:27.67 ___ __ 87629790
GNI 1.48 213.2 18:26:09.1 215.0 ___ __ 85737847
GNI 1.48 213.2 P 18:26:09.0 ___ _i 85738129
GNI 1.48 213.2 Pg 18:26:08.995 347.5 1.80 ___ 3609 1597.1 0.33 __ 87770954
GNI 1.48 213.2 Lg 18:26:28.495 127.0 22.90 ___ 8.4 4590.5 0.33 __ 87770955
GNI 1.48 213.2 LR 18:26:55.856 24.0 51.90 ___ 765.7 18.31 __ 87770956
GNI 1.48 213.2 P 18:26:08.92 ___ di 87861228
GNI 1.48 213.2 S 18:26:29.27 ___ di 87861229
BRNG 1.50 279.3 Pb 18:26:08.37 0.6 ___ __ 87629785
BRNG 1.50 279.3 S 18:26:28.69 ___ __ 87629786
PNSH 1.52 324.8 Pb 18:26:09.26 1.2 ___ __ 87629799
PNSH 1.52 324.8 S 18:26:29.61 ___ __ 87629800
...
Closest station DDFL with a large reported residual

## Slide 29: Exercises
Sta Dist EvAz Phase Time TRes Azim AzRes Slow SRes Def SNR Amp Per Qual Magnitude ArrID
...
ALIG 1.76 294.4 Pb 18:26:12.2 0.1 ___ __ 87629779
ALIG 1.76 294.4 S 18:26:35.69 ___ __ 87629780
METS 1.81 226.9 Pg 18:26:13.92 0.4 ___ __ 87629795
METS 1.81 226.9 S 18:26:36.88 ___ __ 87629796
METS 1.81 226.9 P 18:26:13.85 ___ ci 87861238
METS 1.81 226.9 S 18:26:37.43 ___ ci 87861239
GRO 1.92 358.9 P 18:26:15.2 ___ _i 85738131
GRS 1.94 167.8 P 18:26:16.24 ___ ci 87861234
GRS 1.94 167.8 S 18:26:41.29 ___ ci 87861235
VNNZ 1.98 230.0 P 18:26:17.61 ___ di 87861242
VNNZ 1.98 230.0 S 18:26:43.91 ___ ci 87861243
ZEI 1.98 315.1 P 18:26:16.6 ___ _e 85738132
DRN 2.00 70.7 P 18:26:17.4 ___ _i 85738134
MAK 2.01 38.4 P 18:26:18.0 ___ _i 85738133
ONI 2.12 305.0 P 18:26:17.8 ___ _e 85738135
ONI 2.12 305.0 Pb 18:26:17.62 0.6 ___ __ 87629797
ONI 2.12 305.0 S 18:26:48.17 ___ __ 87629798
ABS 2.27 280.1 Pb 18:26:19.42 1.4 ___ __ 87629777
ABS 2.27 280.1 S 18:26:51.36 ___ __ 87629778
TKB 2.30 295.4 Pb 18:26:19.93 1.4 ___ __ 87629805
TKB 2.30 295.4 S 18:26:52.13 ___ __ 87629806
NCK 2.66 322.8 P 18:26:23.3 ___ _e 85738136
NEY 2.94 310.0 P 18:26:29.5 ___ _e 85738137
BATM 3.09 275.2 Pn 18:26:31.4 2.4 ___ __ 87629781
BATM 3.09 275.2 S 18:27:16.32 ___ __ 87629782
KBZ 3.17 318.3 P 18:26:30.7 ___ _i 85738138
KBZ 3.17 318.3 Pn 18:26:33.525 184.9 9.30 ___ 40.3 9.4 0.33 __ ML 3.7 87770968
KBZ 3.17 318.3 Pg 18:26:38.475 147.7 12.10 ___ 85.9 84.9 0.33 __ 87770969
KBZ 3.17 318.3 Lg 18:27:19.825 324.3 19.50 ___ 13.4 109.1 0.33 __ 87770970
KBZ 3.17 318.3 ___ 59.1 0.50 __ mbtmp 4.1 87770971
KVAR 3.43 319.2 Pn 18:26:36.351 275.7 22.80 ___ __ ML 3.1 87770985
KVAR 3.43 319.2 Pg 18:26:43.626 99.5 22.80 ___ __ 87770986
KVAR 3.43 319.2 Lg 18:27:28.851 137.7 12.60 ___ __ 87770987
KVAR 3.43 319.2 ___ 6.2 0.44 __ mbtmp 3.3 87770988
KIV 3.44 319.1 18:26:36.5 315.0 ___ __ 85737848
KIV 3.44 319.1 P 18:26:33.8 ___ ci 85738139
RPOR 4.69 301.2 P 18:26:52.6 ___ _i 85738140
Duplicate readings from stations that are picked/reported by several agencies
Can’t tell who picked and who reported the phase

## Slide 30: Exercises
Sta Dist EvAz Phase Time TRes Azim AzRes Slow SRes Def SNR Amp Per Qual Magnitude ArrID
ARCR 16.37 297.5 P 18:29:37.0 ___ 14.8 1.26 a__ 85737766
ARCR 16.37 297.5 P 18:29:37.0 ___ 14.8 1.26 a__ 85737776
ARCR 16.37 297.5 P 18:29:37.0 ___ 14.8 1.26 a__ 85737787
ARCR 16.37 297.5 P 18:29:37.0 ___ 11759.2 a__ 85737804
ARCR 16.37 297.5 P 18:29:37.0 ___ 11759.2 a__ 85737823
ARCR 16.37 297.5 18:29:33.3 297.0 ___ 14.8 1.30 __ 85737868
ARCR 16.37 297.5 P 18:29:37.0 ___ 11759.2 a__ 85737905
ARCR 16.37 297.5 P 18:29:37.0 ___ 11759.2 a__ 85829156
ZKR 16.60 254.2 18:29:33.7 254.0 ___ 39.7 0.90 __ 85737869
CJR 16.80 295.9 P 18:29:42.4 ___ 59.0 1.12 a__ 85737768
CJR 16.80 295.9 P 18:29:42.4 ___ 716.4 a__ 85737778
CJR 16.80 295.9 P 18:29:42.4 ___ 716.4 a__ 85737789
CJR 16.80 295.9 P 18:29:42.4 ___ 716.4 a__ 85737805
CJR 16.80 295.9 P 18:29:42.4 ___ 716.4 a__ 85737824
CJR 16.80 295.9 P 18:29:42.4 ___ 716.4 a__ 85737906
CJR 16.80 295.9 P 18:29:35.8 ___ 718.8 m__ 85829157
CJR 16.80 295.9 P 18:29:39.045 1.2 ___ c_ 87432866
VTS 16.81 281.7 P 18:29:39.4 ___ 27.9 0.99 a__ 85737767
VTS 16.81 281.7 P 18:29:39.4 ___ 27.9 0.99 a__ 85737777
VTS 16.81 281.7 P 18:29:39.4 ___ 27.9 0.99 a__ 85737788
VTS 16.81 281.7 P 18:29:39.4 ___ 27.9 0.99 a__ 85737806
VTS 16.81 281.7 P 18:29:39.4 ___ 27.9 0.99 a__ 85737825
VTS 16.81 281.7 18:29:39.0 281.0 ___ 27.3 1.00 __ 85737871
VTS 16.81 281.7 P 18:29:39.4 ___ 27.9 0.99 a__ 85737907
VTS 16.81 281.7 P 18:29:39.4 ___ 27.9 0.99 a__ 85829158
VTS 16.81 281.7 P 18:29:35.972 2.1 ___ d_ 87432865
...
GZR 17.19 291.2 P 18:29:43.3 ___ 13.5 1.36 a__ 85737770
GZR 17.19 291.2 P 18:29:43.3 ___ 13.5 1.36 a__ 85737779
GZR 17.19 291.2 P 18:29:43.3 ___ 13.5 1.36 a__ 85737790
GZR 17.19 291.2 P 18:29:43.3 ___ 13.5 1.36 a__ 85737807
GZR 17.19 291.2 P 18:29:43.3 ___ 13.5 1.36 a__ 85737826
GZR 17.19 291.2 P 18:29:43.3 ___ 13.5 1.36 a__ 85737908
GZR 17.19 291.2 P 18:29:43.3 ___ 13.5 1.36 a__ 85829159
GZR 17.19 291.2 P 18:29:42.863 0.8 ___ c_ 87432869
Duplicate readings represent perfectly correlated picks
They could introduce location bias
iLoc takes care of this

## Slide 31: Heavily unbalanced network

## Slide 32: Exercises
Sta Dist EvAz Phase Time TRes Azim AzRes Slow SRes Def SNR Amp Per Qual Magnitude ArrID
NACGM 18.45 323.5 P 18:29:55.63 0.3 ___ _e 87626052
NACGM 18.45 323.5 P 18:29:55.63 ___ 11.0 0.85 _e 87626053
NACGM 18.45 323.5 P 18:29:56.16 ___ _e 87626054
NACGM 18.45 323.5 PP 18:30:08.24 ___ _e 87626055
NACGM 18.45 323.5 PPP 18:30:22.27 ___ _e 87626056
NACGM 18.45 323.5 S 18:33:19.03 ___ __ 87626057
NACGM 18.45 323.5 SS 18:33:33.79 ___ __ 87626058
NACGM 18.45 323.5 SSS 18:33:50.05 ___ __ 87626059
NACGM 18.45 323.5 LQ 18:35:29.14 ___ __ 87626060
NACGM 18.45 323.5 LR 18:36:22.75 ___ __ 87626061
NACGM 18.45 323.5 LRM 18:37:34.1 ___ 245.0 18.50 __ 87626062
NACGM 18.45 323.5 LRM 18:38:10.14 ___ 6218.0 18.25 __ 87626063
NACGM 18.45 323.5 LRM 18:38:13.67 ___ 6566.0 18.13 __ 87626064
...
LZH 44.86 77.0 P 18:33:56.3 ___ _e 24107223
LZH 44.86 77.0 pP 18:34:03.7 ___ __ 24107224
LZH 44.86 77.0 sP 18:34:07.4 ___ __ 24107225
LZH 44.86 77.0 pmax ___ 24.0 1.10 __ 24107226
LZH 44.86 77.0 LR ___ 220.0 15.80 __ 24107227
LZH 44.86 77.0 LR ___ 160.0 16.60 __ 24107228
LZH 44.86 77.0 LR ___ 250.0 15.80 __ 24107229
XAN 49.49 76.9 P 18:34:31.0 ___ d_ 24107244
XAN 49.49 76.9 pP 18:34:35.8 ___ __ 24107245
XAN 49.49 76.9 S 18:41:38.9 ___ __ 24107246
XAN 49.49 76.9 sS 18:41:46.8 ___ __ 24107247
XAN 49.49 76.9 pmax ___ 23.0 0.90 __ 24107248
XAN 49.49 76.9 pmax ___ 110.0 4.50 __ 24107249
HEH 54.86 51.0 P 18:35:10.7 ___ __ 24107211
HEH 54.86 51.0 sP 18:35:20.7 ___ __ 24107212
HEH 54.86 51.0 PcP 18:36:15.9 ___ __ 24107213
HEH 54.86 51.0 pmax ___ 5.0 0.60 __ 24107214
...
CN2 56.48 58.7 P 18:35:22.5 ___ _e 24107202
CN2 56.48 58.7 PP 18:37:29.2 ___ _e 24107203
CN2 56.48 58.7 S 18:43:09.7 ___ _e 24107204
CN2 56.48 58.7 LR ___ 250.0 22.00 __ 24107205
CN2 56.48 58.7 LR ___ 160.0 22.00 __ 24107206
CN2 56.48 58.7 LR ___ 120.0 23.00 __ 24107207
Overly eager analysts are prone to pick predicted phases

## Slide 33: Exercises
Sta Dist EvAz Phase Time TRes Azim AzRes Slow SRes Def SNR Amp Per Qual Magnitude ArrID
USRK 60.42 55.6 P 18:35:49.25 280.7 7.50 ___ 6.2 0.9 0.52 __ mbtmp 4.0 87771021
USRK 60.42 55.6 ___ 0.9 0.52 __ mb 4.0 87771022
SEY 60.82 30.1 P 18:35:53.3 ___ ce 85738159
KSRS 61.25 64.0 P 18:35:55.4 294.5 6.90 ___ 6.6 1.5 0.63 __ mbtmp 4.1 87770979
KSRS 61.25 64.0 LR 19:02:45.797 280.0 36.40 ___ 47.8 19.90 __ MS 3.6 87770980
KSRS 61.25 64.0 ___ 1.5 0.63 __ mb 4.1 87770981
MA2 62.08 33.8 LR 19:04:55.521 302.0 38.00 ___ 55.7 18.83 __ MS 3.7 87770990
FRB 63.12 333.0 LR 19:04:34.207 190.0 37.00 ___ 60.0 19.25 __ MS 3.7 87770949
JNU 65.64 66.6 LR 19:07:58.301 300.0 38.70 ___ 59.8 19.29 __ MS 3.7 87770966
TSUM 65.72 209.4 LR 19:05:00.122 141.0 35.90 ___ 84.2 18.10 __ MS 3.9 87771020
ASAJ 66.87 51.1 LR 19:09:42.812 185.5 39.50 ___ 58.5 18.34 __ MS 3.8 87770964
MJAR 68.59 59.8 LR 19:08:25.802 314.5 37.40 ___ 84.8 21.30 __ MS 3.9 87770992
LBTB 68.68 199.7 LR 19:10:05.233 173.5 38.80 ___ 154.7 19.78 __ MS 4.2 87770989
PETK 69.12 36.8 LR 19:14:11.492 300.1 42.10 ___ 42.8 18.08 __ MS 3.7 87771010
ILAR 73.70 5.6 LR 19:13:29.164 257.5 38.90 ___ 23.8 18.01 __ MS 3.4 87770963
YKA 75.27 350.7 P 18:37:24.225 12.5 8.90 ___ 3.6 0.3 0.51 __ mbtmp 3.6 87771029
YKA 75.27 350.7 LR 19:12:07.3 335.5 37.10 ___ 38.7 19.02 __ MS 3.6 87771030
YKA 75.27 350.7 ___ 0.3 0.51 __ mb 3.6 87771031
DAV 77.70 91.4 LR 19:14:15.043 43.5 37.50 ___ 63.9 20.40 __ MS 3.8 87770937
KDAK 79.99 9.9 LR 19:17:22.663 23.4 38.80 ___ 42.6 18.05 __ MS 3.7 87770972
KAPI 81.37 104.5 LR 19:24:21.74 266.0 43.30 ___ 90.1 18.23 __ MS 4.1 87770967
BBB 86.65 356.3 LR 19:22:21.61 21.5 39.30 ___ 29.6 18.89 __ MS 3.6 87770924
GUMO 87.79 73.9 LR 19:21:09.51 357.5 37.90 ___ 13.0 20.45 __ MS 3.2 87770957
PDAR 93.32 342.1 LR 19:22:45.597 31.0 36.70 ___ 27.8 18.20 __ MS 3.6 87771009
YBH 96.60 351.4 LR 19:25:39.879 334.0 37.30 ___ 46.9 18.13 __ MS 3.9 87771028
NVAR 99.24 347.4 LR 19:25:38.52 45.0 36.30 ___ 25.1 19.66 __ MS 3.6 87771006
GARM 99.29 350.6 18:30:00.7 90.0 ___ 203.3 0.90 __ 85737878
ANMO 99.87 337.2 LR 19:25:29.159 103.5 36.00 ___ 38.5 18.24 __ MS 3.8 87770917
STOP
LR without body wave detections

## Slide 34: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with ak135 predictions (one line!)
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=0 use_RSTT_PgLg=0" | iloc isf > 20170607182541.log
cat 20170607182541.log
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 10.0
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pg 1 2017-06-07 18:25:51.300 0.24 82.48 0.800 00 4.939 ak135
1 87629788 FDSN.IR.DDFL.-- ??? S Sg 0 2017-06-07 18:25:58.760 0.24 82.48 1.500 00 8.758 ak135
2 87629793 FDSN.IR.LGD.-- ??? Pn Pb 1 2017-06-07 18:25:53.310 0.54 38.22 0.800 10 1.184 ak135
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:40.993 Lat = 41.415 Lon = 45.799 Depth = 14.9
etype=uk nreading=229 nass=542 ndef=347 ndefsta=187 nrank=207 sdobs=2.238 sgap= 44.1
smajax=2.9 sminax=2.7 strike=113.0 stime=0.331 sdepth=2.0
depdp=15.00 +/- 3.84 ndp=14
free-depth solution
local network: nsta=8 ndef=14 sgap=215.7 dU=0.421 ndefsta_10km=0 GT5cand=0
mb=4.68 +/- 0.24 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.93 +/- 0.29 nsta=7
mB=5.44 +/- 0.52 nsta=45
Finished event 610666945 (0.21)
EVENT 0.214577 542

## Slide 35: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with ak135 predictions and grid search (one line!)
echo "isf_infile=20170607182541.isf do_gridsearch=1 use_RSTT_PnSn=0 use_RSTT_PgLg=0" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 10.0
Neighbourhood algorithm (0.0089)
Best fitting hypocentre from grid search:
OT = 2017-06-07 18:25:42.228 Lat = 41.593 Lon = 45.827 Depth = 10.0
Distance from initial guess = 21.0 km
…
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg 1 2017-06-07 18:25:51.300 0.23 98.68 0.800 00 ak135
1 87629788 FDSN.IR.DDFL.-- ??? S Sb 0 2017-06-07 18:25:58.760 0.23 98.68 1.500 00 7.491 ak135
2 87629793 FDSN.IR.LGD.-- ??? Pn Pn 1 2017-06-07 18:25:53.310 0.48 41.71 0.800 10 -0.449 ak135
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:41.602 Lat = 41.481 Lon = 45.819 Depth = 16.3
etype=uk nreading=229 nass=542 ndef=361 ndefsta=190 nrank=265 sdobs=2.217 sgap= 42.7
smajax=3.4 sminax=2.9 strike=176.5 stime=0.340 sdepth=1.9
depdp=16.00 +/- 3.84 ndp=14
free-depth solution
local network: nsta=8 ndef=14 sgap=210.1 dU=0.406 ndefsta_10km=0 GT5cand=0
mb=4.68 +/- 0.24 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.94 +/- 0.29 nsta=7
mB=5.43 +/- 0.52 nsta=44
Finished event 610666945 (9.73)
EVENT 9.728229 542

## Slide 36: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with ak135 predictions, no grid search and with initial depth 15km
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=0 use_RSTT_PgLg=0 depth=15" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 15.0
…
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pb 1 2017-06-07 18:25:51.300 0.25 84.01 0.800 10 3.781 ak135
1 87629788 FDSN.IR.DDFL.-- ??? S Sb 0 2017-06-07 18:25:58.760 0.25 84.01 1.500 10 7.176 ak135
2 87629793 FDSN.IR.LGD.-- ??? Pn Pn 1 2017-06-07 18:25:53.310 0.53 39.14 0.800 10 -1.000 ak135
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:41.461 Lat = 41.420 Lon = 45.790 Depth = 17.3
etype=uk nreading=229 nass=542 ndef=353 ndefsta=182 nrank=214 sdobs=2.428 sgap= 43.9
smajax=2.8 sminax=2.7 strike=16.7 stime=0.330 sdepth=1.9
depdp=18.00 +/- 3.84 ndp=16
free-depth solution
local network: nsta=9 ndef=16 sgap=195.5 dU=0.331 ndefsta_10km=0 GT5cand=0
mb=4.67 +/- 0.23 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.92 +/- 0.29 nsta=7
mB=5.39 +/- 0.56 nsta=43
Finished event 610666945 (0.20)
EVENT 0.195679 542

## Slide 37: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with ak135 predictions, no grid search and with initial hypocentre TIF
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=0 use_RSTT_PgLg=0 time=TIF lat=TIF depth=TIF" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.800 Lat = 41.406 Lon = 45.796 Depth = 29.4
Event location
maximum number of iterations is reached!
Fix depth by default depth grid: 12.00
Initial hypocentre:
OT = 2017-06-07 18:25:40.060 Lat = 41.406 Lon = 45.796 Depth = 12.0
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pb 1 2017-06-07 18:25:51.300 0.26 85.77 0.800 10 4.132 ak135
1 87629788 FDSN.IR.DDFL.-- ??? S Sg 0 2017-06-07 18:25:58.760 0.26 85.77 1.500 00 9.174 ak135
2 87629793 FDSN.IR.LGD.-- ??? Pn Pn 1 2017-06-07 18:25:53.310 0.54 40.52 0.800 10 -0.718 ak135
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:40.511 Lat = 41.427 Lon = 45.775 Depth = 12.0
etype=uk nreading=229 nass=542 ndef=346 ndefsta=178 nrank=212 sdobs=2.435 sgap= 43.8
smajax=2.6 sminax=2.5 strike=118.9 stime=0.292
depdp=12.00 +/- 3.80 ndp=14
depth fixed to default depth grid depth
local network: nsta=9 ndef=15 sgap=194.4 dU=0.325 ndefsta_10km=0 GT5cand=0
mb=4.69 +/- 0.25 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.92 +/- 0.29 nsta=7
mB=5.35 +/- 0.47 nsta=44
Finished event 610666945 (0.44)

## Slide 38: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with ak135 predictions, start from TIF and fix depth to TIF
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=0 use_RSTT_PgLg=0 time=TIF lat=TIF fix_depth=TIF" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.800 Lat = 41.406 Lon = 45.796 Depth = 29.4
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pn 1 2017-06-07 18:25:51.300 0.23 81.83 0.800 10 1.446 ak135
1 87629788 FDSN.IR.DDFL.-- ??? S Sb 0 2017-06-07 18:25:58.760 0.23 81.83 1.500 10 5.343 ak135
2 87629793 FDSN.IR.LGD.-- ??? Pn Pn 1 2017-06-07 18:25:53.310 0.53 37.41 0.800 10 -0.596 ak135
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:42.275 Lat = 41.413 Lon = 45.810 Depth = 29.4
etype=uk nreading=229 nass=542 ndef=348 ndefsta=178 nrank=209 sdobs=2.858 sgap= 44.1
smajax=3.0 sminax=2.9 strike=123.9 stime=0.304
depdp=29.00 +/- 4.71 ndp=15
depth fixed to TIF depth
local network: nsta=9 ndef=16 sgap=196.8 dU=0.337 ndefsta_10km=0 GT5cand=0
mb=4.62 +/- 0.20 nsta=50
MS=3.74 +/- 0.14 nsta=44
ML=4.93 +/- 0.29 nsta=7
mB=5.35 +/- 0.55 nsta=44
Finished event 610666945 (0.20)

## Slide 39: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with ak135 predictions, fix hypocentre to TIF
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=0 use_RSTT_PgLg=0 fix_hypo=TIF" | iloc isf
Will not produce a location just calculate the residuals w.r.t. the fixed hypocentre
Useful to assess the quality of travel time predictions
Calculate residuals for fixed hypocentre
Calculating residuals for a fixed hypocentre
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pn 1 2017-06-07 18:25:51.300 0.25 80.50 0.800 10 1.757 ak135
1 87629788 FDSN.IR.DDFL.-- ??? S Sb 0 2017-06-07 18:25:58.760 0.25 80.50 1.500 10 5.578 ak135
2 87629793 FDSN.IR.LGD.-- ??? Pn Pn 1 2017-06-07 18:25:53.310 0.54 37.85 0.800 10 -0.292 ak135
Fits closest station better, but provides poor fit to far-regional and teleseismic stations

## Slide 40: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with RSTT predictions
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=1 use_RSTT_PgLg=1" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 10.0
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pg 1 2017-06-07 18:25:51.300 0.29 84.76 0.800 00 3.600 RSTT
1 87629788 FDSN.IR.DDFL.-- ??? S Lg 0 2017-06-07 18:25:58.760 0.29 84.76 1.500 10 6.180 RSTT
2 87629793 FDSN.IR.LGD.-- ??? Pn Pg 1 2017-06-07 18:25:53.310 0.56 42.09 0.800 10 0.786 RSTT
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:41.105 Lat = 41.420 Lon = 45.741 Depth = 15.5
etype=uk nreading=229 nass=542 ndef=351 ndefsta=192 nrank=206 sdobs=2.349 sgap= 43.9
smajax=3.0 sminax=2.7 strike=134.8 stime=0.335 sdepth=1.9
depdp=16.00 +/- 4.58 ndp=14
free-depth solution
local network: nsta=9 ndef=15 sgap=193.8 dU=0.322 ndefsta_10km=0 GT5cand=0
mb=4.68 +/- 0.24 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.92 +/- 0.29 nsta=7
mB=5.44 +/- 0.54 nsta=44
Finished event 610666945 (0.56)

## Slide 41: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with RSTT predictions and grid search
echo "isf_infile=20170607182541.isf do_gridsearch=1 use_RSTT_PnSn=1 use_RSTT_PgLg=1" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 10.0
Neighbourhood algorithm (0.1323)
Best fitting hypocentre from grid search:
OT = 2017-06-07 18:25:41.789 Lat = 41.568 Lon = 45.830 Depth = 10.0
Distance from initial guess = 18.2 km
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pg 1 2017-06-07 18:25:51.300 0.27 89.93 0.800 10 3.506 RSTT
1 87629788 FDSN.IR.DDFL.-- ??? S Lg 0 2017-06-07 18:25:58.760 0.27 89.93 1.500 10 6.160 RSTT
2 87629793 FDSN.IR.LGD.-- ??? Pn Pg 1 2017-06-07 18:25:53.310 0.53 43.04 0.800 10 1.033 RSTT
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:41.298 Lat = 41.446 Lon = 45.756 Depth = 17.1
etype=uk nreading=229 nass=542 ndef=362 ndefsta=192 nrank=207 sdobs=2.404 sgap= 43.3
smajax=3.0 sminax=2.7 strike=140.8 stime=0.329 sdepth=1.9
depdp=17.00 +/- 3.89 ndp=14
free-depth solution
local network: nsta=9 ndef=16 sgap=192.1 dU=0.313 ndefsta_10km=0 GT5cand=0
mb=4.67 +/- 0.24 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.92 +/- 0.29 nsta=7
mB=5.43 +/- 0.52 nsta=43
Finished event 610666945 (133.93)
EVENT 133.933153 542

## Slide 42: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with RSTT predictions, no grid search and with initial depth 15km
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=1 use_RSTT_PgLg=1 depth=15" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 15.0
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pg 1 2017-06-07 18:25:51.300 0.31 86.48 0.800 10 2.127 RSTT
1 87629788 FDSN.IR.DDFL.-- ??? S Lg 0 2017-06-07 18:25:58.760 0.31 86.48 1.500 10 4.027 RSTT
2 87629793 FDSN.IR.LGD.-- ??? Pn Pg 1 2017-06-07 18:25:53.310 0.57 44.70 0.800 10 -0.278 RSTT
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:41.628 Lat = 41.427 Lon = 45.702 Depth = 21.0
etype=uk nreading=229 nass=542 ndef=357 ndefsta=188 nrank=209 sdobs=2.433 sgap= 43.6
smajax=3.0 sminax=2.8 strike=129.1 stime=0.323 sdepth=3.1
depdp=21.00 +/- 4.60 ndp=15
free-depth solution
local network: nsta=10 ndef=18 sgap=160.9 dU=0.273 ndefsta_10km=0 GT5cand=0
mb=4.66 +/- 0.23 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.91 +/- 0.29 nsta=7
mB=5.39 +/- 0.55 nsta=42
Finished event 610666945 (1.13)
EVENT 1.127983 542

## Slide 43: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with RSTTpredictions, no grid search and with initial hypocentre TIF
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=1 use_RSTT_PgLg=1 time=TIF lat=TIF depth=TIF" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.800 Lat = 41.406 Lon = 45.796 Depth = 29.4
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pg 1 2017-06-07 18:25:51.300 0.29 84.97 0.800 10 2.193 RSTT
1 87629788 FDSN.IR.DDFL.-- ??? S Lg 0 2017-06-07 18:25:58.760 0.29 84.97 1.500 10 4.266 RSTT
2 87629793 FDSN.IR.LGD.-- ??? Pn Pg 1 2017-06-07 18:25:53.310 0.56 42.54 0.800 10 -0.316 RSTT
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:41.799 Lat = 41.421 Lon = 45.733 Depth = 22.6
etype=uk nreading=229 nass=542 ndef=352 ndefsta=187 nrank=213 sdobs=2.485 sgap= 43.9
smajax=3.2 sminax=3.0 strike=5.7 stime=0.340 sdepth=2.2
depdp=23.00 +/- 4.60 ndp=15
free-depth solution
local network: nsta=9 ndef=16 sgap=193.4 dU=0.321 ndefsta_10km=0 GT5cand=0
mb=4.65 +/- 0.23 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.92 +/- 0.29 nsta=7
mB=5.37 +/- 0.53 nsta=45
Finished event 610666945 (0.60)
EVENT 0.596550 542

## Slide 44: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with ak135 predictions, start from TIF and fix depth to TIF
echo "isf_infile=20170607182541.isf do_gridsearch=0 use_RSTT_PnSn=1 use_RSTT_PgLg=1 time=TIF lat=TIF fix_depth=TIF" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.800 Lat = 41.406 Lon = 45.796 Depth = 29.4
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pg 1 2017-06-07 18:25:51.300 0.28 85.02 0.800 10 1.099 RSTT
1 87629788 FDSN.IR.DDFL.-- ??? S Lg 0 2017-06-07 18:25:58.760 0.28 85.02 1.500 10 2.886 RSTT
2 87629793 FDSN.IR.LGD.-- ??? Pn Pg 1 2017-06-07 18:25:53.310 0.56 42.12 0.800 10 -1.102 RSTT
...
final : Eastern Caucasus
OT = 2017-06-07 18:25:42.261 Lat = 41.422 Lon = 45.742 Depth = 29.4
etype=uk nreading=229 nass=542 ndef=356 ndefsta=187 nrank=213 sdobs=2.872 sgap= 43.8
smajax=3.1 sminax=3.0 strike=9.0 stime=0.307
depdp=29.00 +/- 4.71 ndp=15
depth fixed to TIF depth
local network: nsta=9 ndef=16 sgap=193.7 dU=0.322 ndefsta_10km=0 GT5cand=0
mb=4.62 +/- 0.22 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.92 +/- 0.29 nsta=7
mB=5.34 +/- 0.52 nsta=45
Finished event 610666945 (0.47)

## Slide 45: Exercises: location, location, location
Locate event 2017/07/07, Eastern Caucasus with RSTT predictions, grid search and fix depth to 22 km
echo "isf_infile=20170607182541.isf do_gridsearch=1 use_RSTT_PnSn=1 use_RSTT_PgLg=1 fix_depth=22" | iloc isf
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 22.0
Neighbourhood algorithm (0.1203)
Best fitting hypocentre from grid search:
OT = 2017-06-07 18:25:42.224 Lat = 41.439 Lon = 45.708 Depth = 22.0
Distance from initial guess = 8.5 km
...
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pg 1 2017-06-07 18:25:51.300 0.31 87.51 0.800 10 1.980 RSTT
1 87629788 FDSN.IR.DDFL.-- ??? S Lg 0 2017-06-07 18:25:58.760 0.31 87.51 1.500 10 3.871 RSTT
2 87629793 FDSN.IR.LGD.-- ??? Pn Pg 1 2017-06-07 18:25:53.310 0.57 44.81 0.800 10 -0.332 RSTT
…
final : Eastern Caucasus
OT = 2017-06-07 18:25:41.760 Lat = 41.433 Lon = 45.707 Depth = 22.0
etype=uk nreading=229 nass=542 ndef=368 ndefsta=190 nrank=209 sdobs=2.549 sgap= 43.5
smajax=3.0 sminax=2.9 strike=147.7 stime=0.302
depdp=22.00 +/- 4.64 ndp=16
depth fixed by editor
local network: nsta=10 ndef=18 sgap=159.7 dU=0.271 ndefsta_10km=0 GT5cand=0
mb=4.65 +/- 0.23 nsta=49
MS=3.74 +/- 0.14 nsta=44
ML=4.91 +/- 0.29 nsta=7
mB=5.39 +/- 0.55 nsta=42
Finished event 610666945 (226.61)
EVENT 226.612876 542

## Slide 46: Using a local velocity model
Local velocity model can be specified in config.txt or in the command line, the controlling parameters are
localvmodelfile=full pathname for the local velocity model
max_localTT_delta=3 (the validity range of the local model)
Format for the 1D local velocity model
#
# ak135
#
# depth Vp Vs layername
#
# number of layers
4
0.000 5.8000 3.4600 x
20.000 6.5000 3.8500 CONRAD
35.000 8.0400 4.4800 MOHO
77.500 8.0400 4.4800 x
You can have only one local velocity model specified!

## Slide 47: Using a local velocity model
Locate event 2017/07/07, Eastern Caucasus with local + RSTT + ak135 predictions with the local model valid up to 3 degrees
﻿echo "isf_infile=20170607182541.isf do_gridsearch=1 use_RSTT_PnSn=1 use_RSTT_PgLg=1 localvmodelfile=/Users/istvanbondar/iLocRelease1.60/etc/localmodels/graczer.localmodel.dat max_localTT_delta=3" | iloc isf
﻿
Local velocity model from /Users/istvanbondar/iLocRelease1.60/etc/localmodels/graczer.localmodel.dat
LAYER DEPTH VP VS
0 0.000 5.300 3.046
1 3.000 5.740 3.299
2 19.000 6.290 3.615 CONRAD
3 26.000 7.930 4.558 MOHO
4 77.500 7.930 4.558
read RSTT model: /Users/istvanbondar/SLBM_Root.3.0.5.MacOSX/models/rstt201404um.geotess
RSTT predictions for Pn/Sn Pg/Lg will be used.
Initial hypocentre:
OT = 2017-06-07 18:25:41.000 Lat = 41.406 Lon = 45.800 Depth = 10.0
Neighbourhood algorithm (0.1021)
Best fitting hypocentre from grid search:
OT = 2017-06-07 18:25:40.342 Lat = 41.377 Lon = 45.841 Depth = 5.2
Distance from initial guess = 4.7 km

## Slide 48: Using a local velocity model
RDID ARRID STA PCH REPORTED IASPEI I TIME DELTA ESAZ DELTIM TF RESIDUAL MTYPE AMP PER ACH M MODEL
1 87629787 FDSN.IR.DDFL.-- ??? Pg Pn 1 2017-06-07 18:25:51.300 0.25 77.07 0.800 10 2.497 local
1 87629788 FDSN.IR.DDFL.-- ??? S Sn 0 2017-06-07 18:25:58.760 0.25 77.07 1.500 10 3.885 local
2 87629793 FDSN.IR.LGD.-- ??? Pn Pn 1 2017-06-07 18:25:53.310 0.56 36.95 0.800 10 0.262 local
2 87629794 FDSN.IR.LGD.-- ??? S Sb 0 2017-06-07 18:26:02.010 0.56 36.95 1.500 10 0.803 local
3 87629801 FDSN.IR.SEAG.-- ??? Pn Pn 1 2017-06-07 18:25:57.890 0.83 297.01 0.800 10 0.984 local
3 87629802 FDSN.IR.SEAG.-- ??? S Lg 0 2017-06-07 18:26:09.920 0.83 297.01 1.500 10 0.795 local
4 87629791 FDSN.IR.KZRT.-- ??? Pb Pn 1 2017-06-07 18:26:00.460 1.05 270.26 0.800 10 0.503 local
4 87629792 FDSN.IR.KZRT.-- ??? S Sn 0 2017-06-07 18:26:14.520 1.05 270.26 1.500 10 0.235 local
5 87861232 FDSN.IR.STE.-- ??? P Pn 1 2017-06-07 18:26:02.180 1.14 250.53 0.800 10 0.844 local
5 87861233 FDSN.IR.STE.-- ??? S Sn 0 2017-06-07 18:26:17.310 1.14 250.53 1.500 10 0.639 local
6 85738126 FDSN.IR.KMKR.-- ??? P Pb 1 2017-06-07 18:26:04.300 1.22 52.39 0.800 10 -0.013 local
7 87629807 FDSN.IR.TRLG.-- ??? Pb Pn 1 2017-06-07 18:26:04.060 1.28 277.23 0.800 10 0.779 local
7 87629808 FDSN.IR.TRLG.-- ??? S Sn 0 2017-06-07 18:26:21.000 1.28 277.23 1.500 10 0.946 local
8 85738127 FDSN.IR.BTLR.-- ??? P Pb 1 2017-06-07 18:26:06.200 1.31 13.92 0.800 10 0.421 local
10 87861244 FDSN.IR.KAPZ.-- ??? P Pg 1 2017-06-07 18:26:06.490 1.35 218.26 0.800 10 -0.564 local
10 87861245 FDSN.IR.KAPZ.-- ??? S Lg 0 2017-06-07 18:26:25.010 1.35 218.26 1.500 10 -1.595 local
9 87629803 FDSN.IR.SHTL.-- ??? Pb Pb 1 2017-06-07 18:26:06.240 1.35 339.52 0.800 10 -0.292 local
9 87629804 FDSN.IR.SHTL.-- ??? S Sn 0 2017-06-07 18:26:23.880 1.35 339.52 1.500 10 2.096 local
12 87629789 FDSN.IR.GUDG.-- ??? Pb Pb 1 2017-06-07 18:26:08.160 1.46 317.96 0.800 10 -0.221 local
12 87629790 FDSN.IR.GUDG.-- ??? S Sn 0 2017-06-07 18:26:27.670 1.46 317.96 1.500 10 3.283 local
11 85738128 FDSN.IR.AKT.-- ??? P Pb 1 2017-06-07 18:26:07.500 1.46 85.84 0.800 10 -0.865 local
13 87861228 FDSN.IR.GNI.-- ??? P Pb 1 2017-06-07 18:26:08.972 1.48 213.17 0.800 10 0.285 local
13 87770954 FDSN.IR.GNI.-- ??? Pg Pb 0 2017-06-07 18:26:08.972 1.48 213.17 0.800 10 0.285 ML 1597.1 ??? 0 local
13 85738129 FDSN.IR.GNI.-- ??? P Pb 0 2017-06-07 18:26:08.972 1.48 213.17 0.800 10 0.285 local
13 85737847 FDSN.IR.GNI.-- ??? 0 2017-06-07 18:26:09.100 1.48 213.17 0.000 00 null
13 87770955 FDSN.IR.GNI.-- ??? Lg Sb 0 2017-06-07 18:26:28.495 1.48 213.17 1.500 10 -0.935 ML 4590.5 ??? 1 local
13 87861229 FDSN.IR.GNI.-- ??? S Lg 0 2017-06-07 18:26:29.270 1.48 213.17 1.500 10 -1.459 local
13 87770956 FDSN.IR.GNI.-- ??? LR LR 0 2017-06-07 18:26:55.856 1.48 213.17 00 765.7 ??? 0 null
14 87629785 FDSN.IR.BRNG.-- ??? Pb Pn 1 2017-06-07 18:26:08.370 1.50 279.60 0.800 10 2.080 local
14 87629786 FDSN.IR.BRNG.-- ??? S Sn 0 2017-06-07 18:26:28.690 1.50 279.60 1.500 10 3.403 local
...
32 85738136 FDSN.IR.NCK.-- ??? P Pn 1 2017-06-07 18:26:23.300 2.66 323.01 0.800 10 0.896 local
33 85738137 FDSN.IR.NEY.-- ??? P Pn 1 2017-06-07 18:26:29.500 2.94 310.21 0.800 10 3.052 local
34 87629781 FDSN.IR.BATM.-- ??? Pn Pn 1 2017-06-07 18:26:31.400 3.09 275.32 0.800 10 -0.363 RSTT
34 87629782 FDSN.IR.BATM.-- ??? S Sn 0 2017-06-07 18:27:16.320 3.09 275.32 1.500 10 6.288 RSTT
35 85738138 FDSN.IR.KBZ.-- ??? P Pn 1 2017-06-07 18:26:30.700 3.17 318.48 0.800 10 -1.354 RSTT
35 87770968 FDSN.IR.KBZ.-- ??? Pn Pg 0 2017-06-07 18:26:33.525 3.17 318.48 0.800 00 -5.979 ML 9.4 ??? 0 RSTT
35 87770969 FDSN.IR.KBZ.-- ??? Pg Pb 0 2017-06-07 18:26:38.475 3.17 318.48 0.800 10 -1.029 ML 84.9 ??? 0 RSTT
35 87770970 FDSN.IR.KBZ.-- ??? Lg Lg 0 2017-06-07 18:27:19.825 3.17 318.48 1.500 10 -0.711 ML 109.1 ??? 1 RSTT
35 87770971 FDSN.IR.KBZ.-- ??? AMB 0 3.17 318.48 00 59.1 ??? 0 null
36 87770985 FDSN.IR.KVAR.-- ??? Pn Pn 1 2017-06-07 18:26:36.351 3.43 319.32 0.800 10 0.229 RSTT
36 87770986 FDSN.IR.KVAR.-- ??? Pg Pg 0 2017-06-07 18:26:43.626 3.43 319.32 0.800 10 -1.003 RSTT
36 87770987 FDSN.IR.KVAR.-- ??? Lg Lg 0 2017-06-07 18:27:28.851 3.43 319.32 1.500 10 -0.447 RSTT
36 87770988 FDSN.IR.KVAR.-- ??? AMB 0 3.43 319.32 00 6.2 ??? 0 null
37 85738139 FDSN.IR.KIV.-- ??? P Pn 1 2017-06-07 18:26:33.800 3.44 319.24 0.800 10 -2.322 RSTT
37 85737848 FDSN.IR.KIV.-- ??? 0 2017-06-07 18:26:36.500 3.44 319.24 0.000 00 null
38 85738140 FDSN.IR.RPOR.-- ??? P Pn 1 2017-06-07 18:26:52.600 4.69 301.31 0.800 10 -0.905 RSTT
39 85738141 FDSN.IR.VSLR.-- ??? P Pn 1 2017-06-07 18:26:50.600 4.74 297.80 0.800 00 -3.836 RSTT
40 85738142 FDSN.IR.GUZR.-- ??? P Pn 1 2017-06-07 18:26:57.000 4.93 303.79 0.800 10 0.097 RSTT

## Slide 49: Using a local velocity model
final : Eastern Caucasus
OT = 2017-06-07 18:25:40.584 Lat = 41.390 Lon = 45.794 Depth = 11.4
etype=uk nreading=229 nass=542 ndef=355 ndefsta=193 nrank=208 sdobs=2.082 sgap= 44.7
smajax=2.9 sminax=2.7 strike=113.9 stime=0.354 sdepth=2.1
depdp=11.00 +/- 3.87 ndp=13
free-depth solution
local network: nsta=8 ndef=14 sgap=198.1 dU=0.359 ndefsta_10km=0 GT5cand=0
mb=4.69 +/- 0.22 nsta=50
MS=3.74 +/- 0.14 nsta=44
ML=4.92 +/- 0.29 nsta=7
mB=5.47 +/- 0.54 nsta=44
Finished event 610666945 (114.03)
EVENT 114.032893 542

## Slide 50: Location comparisons
ak135
RSTT
local
indepent errors
Depth fixed to TIF